## Slide 1: Block-based storage

## Slide 2: Block-based Storage System
Upon completion of this module, you should be able to:
Describe the components of block-based storage system
Describe traditional and virtual storage provisioning
Describe storage tiering mechanisms
Notes: This module focuses on the key components of a block-based storage system. It details the function of each component, including cache management and protection techniques. This module also focuses on the two storage provisioning methods. Finally, this module focuses on the storage tiering mechanisms.

## Slide 3: Lesson 1: Components of Block-based Storage System
This lesson covers the following topics:
Block-based storage system components
Intelligent cache algorithms
Cache protection mechanisms
Notes: This lesson covers block-based storage system components, intelligent cache algorithms, and cache protection mechanisms.

## Slide 4: What is a Block-based Storage System?
Provides compute system with block-based access to storage
Can be based on scale-up or scale-out architecture
Two components:
  Controller
  Storage
Notes: A block-based storage system provides compute systems with block-level access to the storage volumes. In this environment, the file system is created on the compute systems and data is accessed on a network at the block level. These block-based storage systems can either be based on scale-up or scale-out architecture. The block-based storage system consists of one or more controller(s) and storage. Controllers and storage are discussed next.

## Slide 5: Components of a Controller
Connectivity
Front End
Back End
Cache
Controller
Storage
Compute
Storage
Network
Notes: A controller of a block-based storage system consists of three key components: front end, cache, and back end. An I/O request received from the compute system at the front-end port is processed through cache and back end, to enable storage and retrieval of data from the storage. A read request can be serviced directly from cache if the requested data is found in the cache. In modern intelligent storage systems, front end, cache, and back end are typically integrated on a single board (referred as a storage processor or storage controller).

## Slide 6: Components of a Controller
Front End
Ports
Front-end
Controllers
Connectivity
Front End
Back End
Cache
Controller
Storage
Compute
Storage
Network
Notes: The front end provides the interface between the storage system and the compute system. It consists of two components: front-end ports and front-end controllers. Typically, a front end has redundant controllers for high availability, and each controller contains multiple ports that enable large numbers of compute systems to connect to the intelligent storage system. Each front-end controller has processing logic that executes the appropriate transport protocol, such as Fibre Channel, iSCSI, FICON, or FCoE for storage connections. Front-end controllers route data to and from cache via the internal data bus. When the cache receives the write data, the controller sends an acknowledgment message back to the compute system.

## Slide 7: Components of a Controller
Cache
Connectivity
Front End
Back End
Cache
Controller
Storage
Compute
Storage
Network
Notes: Cache is semiconductor memory where data is placed temporarily to reduce the time required to service I/O requests from the compute system. Cache improves storage system performance by isolating compute systems from the storage (HDDs and SSDs). The performance improvement is significantly higher when the back-end storage is hard disk drive (HDD). In this case, cache improves storage system performance by isolating compute systems from the mechanical delays associated with rotating disks or HDDs. Rotating disks are the slowest component of an intelligent storage system. Data access on rotating disks usually takes several milliseconds because of seek time and rotational latency. Accessing data from cache is fast and typically takes less than a millisecond. On intelligent storage systems, write data is first placed in cache and then written to the storage.

## Slide 8: Read Operation with Cache
Data found in cache
1. Read Request
Data not found in cache
Data found in cache = Read hit
Data not found in cache = Read miss
1. Read Request
2. Data sent to compute system
4. Data sent to compute system
2. Read Request
3. Data copied to cache
Notes: When a compute system issues a read request, the storage controller reads the tag RAM to determine whether the required data is available in cache. If the requested data is found in the cache, it is called a read cache hit or read hit and data is sent directly to the compute system, without any back-end storage operation. This provides a fast response time to the compute system (about a millisecond). If the requested data is not found in cache, it is called a cache miss and the data must be read from the storage. The back end accesses the appropriate storage device and retrieves the requested data. Data is then placed in cache and finally sent to the compute system through the front end. Cache misses increase the I/O response time.
A prefetch or read-ahead algorithm is used when read requests are sequential. In a sequential read request, a contiguous set of associated blocks is retrieved. Several other blocks that have not yet been requested by the compute system can be read from the storage and placed into cache in advance. When the compute system subsequently requests these blocks, the read operations will be read hits. This process significantly improves the response time experienced by the compute system. The intelligent storage system offers fixed and variable prefetch sizes. In fixed prefetch, the intelligent storage system prefetches a fixed amount of data. It is most suitable when compute system I/O sizes are uniform. In variable prefetch, the storage system prefetches an amount of data in multiples of the size of the compute system request. Maximum prefetch limits the number of data blocks that can be prefetched to prevent the storage from being rendered busy with prefetch at the expense of other I/Os.
Read performance is measured in terms of the read hit ratio, or the hit rate, usually expressed as a percentage. This ratio is the number of read hits with respect to the total number of read requests. A higher read hit ratio improves the read performance.

## Slide 9: Write Operation with Cache
Write-through cache
Write-back cache
Cache
Cache
1. Data write
4. Acknowledgment
2. Data write
3. Acknowledgment
3. Data write
4. Acknowledgment
1. Data write
2. Acknowledgment
Notes: Write operations with cache provide performance advantages over writing directly to storage. When an I/O is written to cache and acknowledged, it is completed in less time (from the compute system’s perspective) than it would take to write directly to storage. Sequential writes also offer opportunities for optimization because many smaller writes can be coalesced for larger transfers to storage with the use of cache. A write operation with cache is implemented in the following ways:
Write-through cache: Data is placed in the cache and immediately written to the storage, and an acknowledgment is sent to the compute system. Because data is committed to storage as it arrives, the risks of data loss are low, but the write-response time is longer because of the storage operations.
Write-back cache: Data is placed in cache and an acknowledgment is sent to the compute system immediately. Later, data from several writes are committed (de-staged) to the storage. Write response times are much faster because the write operations are isolated from the storage devices. However, uncommitted data is at risk of loss if cache failures occur.
Cache can be bypassed under certain conditions, such as large size write I/O. In this implementation, if the size of an I/O request exceeds the predefined size, called write aside size, writes are sent to the storage directly to reduce the impact of large writes consuming a large cache space. This is particularly useful in an environment where cache resources are constrained and cache is required for small random I/Os. Cache can be implemented as either dedicated cache or global cache. With dedicated cache, separate sets of memory locations are reserved for reads and writes. In global cache, both reads and writes can use any of the available memory addresses. Cache management is more efficient in a global cache implementation because only one global set of addresses has to be managed.
Global cache allows users to specify the percentages of cache available for reads and writes for cache management. Typically, the read cache is small, but it should be increased if the application being used is read-intensive. In other global cache implementations, the ratio of cache available for reads versus writes is dynamically adjusted based on the workloads.

## Slide 10: Cache Management: Algorithms
Least recently used (LRU)
  Discards data that have not been accessed for a long time
Most recently used (MRU)
  Discards data that have been most recently accessed
New Data
LRU/MRU Data
Cache
Notes: Cache is an expensive resource that needs proper management. Even though modern intelligent storage systems come with a large amount of cache, when all cache pages are filled, some pages have to be freed up to accommodate new data and avoid performance degradation. Various cache management algorithms are implemented in intelligent storage systems to proactively maintain a set of free pages and a list of pages that can be potentially freed up whenever required.
The most commonly used algorithms are discussed in the following list:
Least Recently Used (LRU): An algorithm that continuously monitors data access in cache and identifies the cache pages that have not been accessed for a long time. LRU either frees up these pages or marks them for reuse. This algorithm is based on the assumption that data that has not been accessed for a while will not be requested by the compute system. However, if a page contains write data that has not yet been committed to storage, the data is first written to the storage before the page is reused.
Most Recently Used (MRU): This algorithm is the opposite of LRU, where the pages that have been accessed most recently are freed up or marked for reuse. This algorithm is based on the assumption that recently accessed data may not be required for a while.

## Slide 11: Cache Management: Watermarking
Manages I/O burst through flushing process
  Flushing is the process of committing data from cache to the storage drives
Three modes of flushing to manage cache utilization are:
  Idle flushing
  High watermark flushing
  Forced flushing
Idle flushing
High watermark flushing
Forced flushing
100%
HWM
LWM
Notes: As cache fills, the storage system must take action to flush dirty pages (data written into the cache but not yet written to the storage) to manage space availability. Flushing is the process that commits data from cache to the storage. On the basis of the I/O access rate and pattern, high and low levels called watermarks are set in cache to manage the flushing process. High watermark (HWM) is the cache utilization level at which the storage system starts high-speed flushing of cache data. Low watermark (LWM) is the point at which the storage system stops flushing data to the storage drives. The cache utilization level drives the mode of flushing to be used:
Idle flushing: It occurs continuously, at a modest rate, when the cache utilization level is between the high and the low watermark.
High watermark flushing: It is activated when cache utilization hits the high watermark. The storage system dedicates some additional resources for flushing. This type of flushing has some impact on I/O processing.
Forced flushing: It occurs in the event of a large I/O burst when cache reaches 100 percent of its capacity, which significantly affects the I/O response time. In forced flushing, system flushes the cache on priority by allocating more resources.
The rate of flushing and the rate of acceptance of compute system I/O into cache is managed dynamically to optimize the storage system performance. The controller dynamically auto-adjusts the incoming and outgoing I/O. The intelligent flushing algorithms provide the storage drives with the time needed to process an increased flushing load by delaying compute system I/O acknowledgments, thus slowing the rate of incoming writes. Throttling continues until the rate of incoming data is equated with the abilities of the underlying storage drives to handle the workload.

## Slide 12: Cache Data Protection
Protects data in the cache against power or cache failures:
  Cache mirroring
    Provides protection to data against cache failure
    Each write to the cache is held in two different memory locations on two independent memory cards
  Cache vaulting
    Provides protection to data against power failure
    In the event of power failure, uncommitted data is dumped to a dedicated set of drives called vault drives
Notes: Cache is volatile memory; so a power failure or any kind of cache failure will cause loss of the data that is not yet committed to the storage drive. This risk of losing uncommitted data held in cache can be mitigated using cache mirroring and cache vaulting:
Cache mirroring: Each write to cache is held in two different memory locations on two independent memory cards. If a cache failure occurs, the write data will still be safe in the mirrored location and can be committed to the storage drive. Reads are staged from the storage drive to the cache; therefore, if a cache failure occurs, the data can still be accessed from the storage drives. Because only writes are mirrored, this method results in better utilization of the available cache. In cache mirroring approaches, the problem of maintaining cache coherency is introduced. Cache coherency means that data in two different cache locations must be identical at all times. It is the responsibility of the storage system's operating environment to ensure coherency.
Cache vaulting: The risk of data loss due to power failure can be addressed in various ways: powering the memory with a battery until the AC power is restored or using battery power to write the cache content to the storage drives. If an extended power failure occurs, using batteries is not a viable option. This is because in intelligent storage systems, large amounts of data might need to be committed to numerous storage drives, and batteries might not provide power for sufficient time to write each piece of data to its intended storage drive. Therefore, storage vendors use a set of physical storage drives to dump the contents of cache during power failure. This is called cache vaulting and the storage drives are called vault drives. When power is restored, data from these storage drives is written back to write cache and then written to the intended drives.

## Slide 13: Lesson 1: Summary
During this lesson the following topics were covered:
Components of block-based storage system
Intelligent cache algorithms
Cache protection mechanisms
Notes: This lesson covered block-based storage system components, intelligent cache algorithms, and cache protection mechanisms.

## Slide 14: Lesson 2: Storage Provisioning
This lesson covers the following topics:
Traditional and virtual provisioning
LUN expansion
LUN masking
Notes: This lesson covers traditional and virtual provisioning processes. This lesson also covers LUN expansion and LUN masking mechanisms.

## Slide 15: Overview of Storage Provisioning
Can be performed in two ways:
  Traditional storage provisioning
  Virtual storage provisioning
The process of assigning storage resources to compute system based on capacity, availability, and performance requirements.
Storage Provisioning
Notes: Storage provisioning is the process of assigning storage resources to compute systems based on capacity, availability, and performance requirements. Storage provisioning can be performed in two ways: traditional and virtual. Virtual provisioning leverages virtualization technology for provisioning storage for applications.

## Slide 16: Traditional Provisioning
Front End
Back End
Cache
Controller
Storage
(RAID Set)
Storage
Network
LUN 0
LUN 1
LUN 0
LUN 1
Compute 1
Compute 2
Notes: In traditional storage provisioning, physical storage drives are logically grouped together on which a required RAID level is applied to form a set, called RAID set. The number of drives in the RAID set and the RAID level determine the availability, capacity, and performance of the RAID set. It is highly recommend to create the RAID set from drives of the same type, speed, and capacity to ensure maximum usable capacity, reliability, and consistency in performance. For example, if drives of different capacities are mixed in a RAID set, the capacity of the smallest drive is used from each drive in the set to make up the RAID set’s overall capacity. The remaining capacity of the larger drives remains unused. Likewise, mixing higher speed drives with lower speed drives lowers the overall performance of the RAID set.
RAID sets usually have a large capacity because they combine the total capacity of individual drives in the set. Logical units are created from the RAID sets by partitioning (seen as slices of the RAID set) the available capacity into smaller units. These units are then assigned to the compute system based on their storage requirements. Logical units are spread across all the physical drives that belong to that set. Each logical unit created from the RAID set is assigned a unique ID, called a logical unit number (LUN). LUNs hide the organization and composition of the RAID set from the compute systems. LUNs created by traditional storage provisioning methods are also referred to as thick LUNs to distinguish them from the LUNs created by virtual provisioning methods.
The figure on the slide shows a RAID set consisting of five storage drives that have been sliced or partitioned into two LUNs: LUN 0 and LUN 1. These LUNs are then assigned to Compute 1 and Compute 2 for their storage requirements.
When a LUN is configured and assigned to a non-virtualized compute system, a bus scan is required to identify the LUN. This LUN appears as a raw storage drive to the operating system. To make this drive usable, it is formatted with a file system and then the file system is mounted.
(Cont’d)

## Slide 17: LUN Expansion
Created by combining two or more LUNs
MetaLUNs can either be concatenated or striped
Concatenated metaLUN
  Provides only additional capacity but no performance
  Expansion is quick as data is not restriped
Striped metaLUN
  Provides capacity and performance
  Expansion is slow as data is restriped
A method to expand LUNs that require additional capacity or performance.
MetaLUN
Notes: MetaLUN is a method to expand LUNs that require additional capacity or performance. A metaLUN can be created by combining two or more LUNs. A metaLUN consists of a base LUN and one or more component LUNs. MetaLUNs can be either concatenated or striped.
Concatenated expansion simply adds additional capacity to the base LUN. In this expansion, the component LUNs are not required to be of the same capacity as the base LUN. All LUNs in a concatenated metaLUN must be either protected (parity or mirrored) or unprotected (RAID 0). RAID types within a metaLUN can be mixed. For example, a RAID 1/0 LUN can be concatenated with a RAID 5 LUN. However, a RAID 0 LUN can be concatenated only with another RAID 0 LUN. Concatenated expansion is quick but does not provide any performance benefit.
Striped expansion restripes the base LUN’s data across the base LUN and component LUNs. In striped expansion, all LUNs must be of the same capacity and RAID level. Striped expansion provides improved performance due to the increased number of drives being striped.
All LUNs in both concatenated and striped expansion must reside on the same storage drive type: either all SSDs, Fibre Channel, or all ATA.

## Slide 18: Virtual Provisioning
Front End
Back End
Cache
Controller
Storage
(Storage Pool)
Storage
Network
Compute 1
Compute 2
Compute System
Reported Capacity
10 TB
3 TB
Allocated
Thin LUN 0
4 TB
Allocated
10 TB
Compute System
Reported Capacity
Thin
LUN 1
Thin
LUN 0
Thin
LUN 1
Notes: Virtual provisioning enables creating and presenting a LUN with more capacity than is physically allocated to it on the storage system. The LUN created using virtual provisioning is called a thin LUN to distinguish it from the traditional LUN.
Thin LUNs do not require physical storage to be completely allocated to them at the time they are created and presented to a compute system. Physical storage is allocated to the compute system “on-demand” from a shared pool of physical capacity. A shared pool consists of physical storage drives. A shared pool in virtual provisioning is analogous to a RAID set, which is a collection of drives on which LUNs are created. Similar to a RAID set, a shared pool supports a single RAID protection level. However, unlike a RAID set, a shared pool might contain large numbers of drives. Shared pools can be homogeneous (containing a single drive type) or heterogeneous (containing mixed drive types, such as SSD, FC, SAS, and SATA drives).
Virtual provisioning enables more efficient allocation of storage to compute systems. Virtual provisioning also enables oversubscription, where more capacity is presented to the compute systems than is actually available on the storage system. Both the shared pool and the thin LUN can be expanded non-disruptively as the storage requirements of the compute systems grow. Multiple shared pools can be created within a storage system, and a shared pool may be shared by multiple thin LUNs.

## Slide 19: Expanding Thin LUNs
Thin LUN
Thin LUN
User capacity before expansion
Adding storage drives to the storage pool
Storage Pool
Storage Pool
Thin pool rebalancing
Thin LUN expansion
User capacity after expansion
Storage Pool Expansion
Thin LUN Expansion
In-use
capacity
In-use
capacity
Notes: A storage pool comprises physical drives that provide the physical storage used by Thin LUNs. A storage pool is created by specifying a set of drives and a RAID type for that pool. Thin LUNs are then created out of that pool (similar to traditional LUN created on a RAID set). All the Thin LUNs created from a pool share the storage resources of that pool. Adding drives to a storage pool increases the available shared capacity for all the Thin LUNs in the pool. Drives can be added to a storage pool while the pool is used in production. The allocated capacity is reclaimed by the pool when Thin LUNs are destroyed.
When a storage pool is expanded, the sudden introduction of new empty drives combined with relative full drives cause a data imbalance. This imbalance is resolved by automating a one-time data relocation, referred to as rebalancing. Storage pool rebalancing is a technique that provides the ability to automatically relocate extents (minimum amount of physical storage capacity that is allocated to the thin LUN from the pool) on physical storage drives over the entire pool when new drives are added to the pool. Storage pool rebalancing restripes data across all the drives( both existing and new drives) in the storage pool. This enables spreading out the data equally on all the physical drives within the storage pool, ensuring that the used capacity of each drive is uniform across the pool. After the storage pool capacity is increased, the capacity of the existing LUNs can be expanded.

## Slide 20: Traditional Provisioning Vs. Virtual Provisioning
Virtual Provisioning
350 GB
Actual data
1650 GB
or
1.65 TB
Available
Capacity
100 GB Allocated
50 GB Allocated
200 GB Allocated
Thin LUN 1
Thin LUN 2
Thin LUN 3
500 GB
550 GB
800 GB
Storage System 2 TB
Traditional Provisioning
350 GB
Actual data
1500 GB
or
1.5 TB
Allocated
Unused
Capacity
400 GB
Allocated
Unused
Capacity
100 GB Data
500 GB
Allocated
Unused
Capacity
50 GB Data
200 GB Data
600 GB
Allocated
Unused
Capacity
LUN 1 500 GB
LUN 2 550 GB
LUN 3 800 GB
Storage System 2 TB
150 GB
Available
Capacity
Notes: Administrators typically allocate storage capacity based on anticipated storage requirements. This generally results in the over provisioning of storage capacity, which then leads to higher costs and lower capacity utilization. Administrators often over-provision storage to an application for various reasons such as, to avoid frequent provisioning of storage if the LUN capacity is exhausted, and to reduce disruption to application availability. Over provisioning of storage often leads to additional storage acquisition and operational costs.
Virtual provisioning addresses these challenges. Virtual provisioning improves storage capacity utilization and simplifies storage management. The figure on the slide illustrates an example, comparing virtual provisioning with traditional storage provisioning.
With traditional provisioning, three LUNs are created and presented to one or more compute systems. The total storage capacity of the storage system is 2 TB. The allocated capacity of LUN 1 is 500 GB, of which only 100 GB is consumed, and the remaining 400 GB is unused. The size of LUN 2 is 550 GB, of which 50 GB is consumed, and 500 GB is unused. The size of LUN 3 is 800 GB, of which 200 GB is consumed, and 600 GB is unused. In total, the storage system has 350 GB of data, 1.5 TB of allocated but unused capacity, and only 150 GB of remaining capacity available for other applications.
Now consider the same 2 TB storage system with virtual provisioning. Here, three thin LUNs of the same sizes are created. However, there is no allocated unused capacity. In total, the storage system with virtual provisioning has the same 350 GB of data, but 1.65 TB of capacity is available for other applications, whereas only 150 GB is available in traditional storage provisioning.
(Cont’d)

## Slide 21: LUN Masking
Implemented on storage system
Prevents unauthorized or accidental use of LUNs in a shared environment
A process that provides data access control by defining which LUNs a compute system can access.
LUN Masking
Notes: LUN masking is a process that provides data access control by defining which LUNs a compute system can access. The LUN masking function is implemented on the storage system. This ensures that volume access by compute system is controlled appropriately, preventing unauthorized or accidental use in a shared environment.
For example, consider a storage system with two LUNs that store data of the sales and finance departments. Without LUN masking, both departments can easily see and modify each other’s data, posing a high risk to data integrity and security. With LUN masking, LUNs are accessible only to the designated compute systems.

## Slide 22: Lesson 2: Summary
During this lesson the following topics were covered:
Traditional and virtual provisioning
LUN expansion
LUN masking
Notes: This lesson covered traditional provisioning, virtual provisioning, LUN expansion, and LUN masking.

## Slide 23: Lesson 3: Storage Tiering
This lesson covers the following topics:
LUN and Sub-LUN tiering
Cache tiering
Server flash caching
Notes: This lesson covers LUN and sub-LUN tiering, cache tiering, and server flash caching.

## Slide 24: Storage Tiering Overview
Each tier has different levels of protection, performance, and cost
Efficient storage tiering requires defining tiering policies
Tiering in block-based storage systems
  LUN and sub-LUN tiering
  Cache tiering
  Server flash-caching
A technique of establishing a hierarchy of storage types and identifying the candidate data to relocate to the appropriate storage type to meet service level requirements at a minimal cost.
Storage Tiering
Notes: Storage tiering is a technique of establishing a hierarchy of different storage types (tiers). This enables storing the right data to the right tier, based on service level requirements, at a minimal cost. Each tier has different levels of protection, performance, and cost. For example, high performance solid-state drives (SSDs) or FC drives can be configured as tier 1 storage to keep frequently accessed data and low cost SATA drives as tier 2 storage to keep the less frequently accessed data. Keeping frequently used data in SSD or FC improves application performance. Moving less-frequently accessed data to SATA can free up storage capacity in high performance drives and reduce the cost of storage. This movement of data happens based on defined tiering policies. The tiering policy might be based on parameters, such as frequency of access. For example, if a policy states “move the data that are not accessed for the last 30 mins to the lower tier,” then all the data matching this condition are moved to the lower tier.
The process of moving the data from one type of tier to another is typically automated. In automated storage tiering, the application workload is proactively monitored; the active data is automatically moved to a higher performance tier and the inactive data is moved to higher capacity, lower performance tier. The data movement between the tiers is performed non-disruptively.
There are three techniques of storage tiering implemented in a block-based storage system: LUN and sub-LUN tiering, cache tiering, and server flash-caching.

## Slide 25: LUN and Sub-LUN Tiering
LUN tiering
  Moves entire LUN from one tier to another
  Does not give effective cost and performance benefits
Sub-LUN tiering
  A LUN is broken down into smaller segments and tiered at that level
  Provides effective cost and performance benefits
Tier 0
Tier 1
LUN Tiering
Move entire LUN
with active data
from tier 1 to tier
0 for improved
performance
Move entire LUN
with inactive
data from
tier 0 to tier 1
Sub-LUN Tiering
Move active data from tier 1 to tier 0 for improved performance
Move inactive data from tier 0 to tier 1
Inactive Data
Active Data
LUN
LUN
LUN
LUN
Tier 1
Tier 0
Notes: The process of storage tiering within a storage system is called intra-array storage tiering. It enables the efficient use of SSD, FC, and SATA drives within a system and provides performance and cost optimization. The goal is to keep the SSDs busy by storing the most frequently accessed data on them, while moving out the less frequently accessed data to the SATA drives. Data movements executed between tiers can be performed at the LUN level or at the sub-LUN level. The performance can be further improved by implementing tiered cache.
Traditionally, storage tiering is operated at the LUN level that moves an entire LUN from one tier of storage to another. This movement includes both active and inactive data in that LUN. This method does not give effective cost and performance benefits. Today, storage tiering can be implemented at the sub-LUN level. In sub-LUN level tiering, a LUN is broken down into smaller segments and tiered at that level. Movement of data with much finer granularity, for example 8 MB, greatly enhances the value proposition of automated storage tiering. Tiering at the sub-LUN level effectively moves active data to faster drives and less active data to slower drives.

## Slide 26: Cache Tiering
Enables creation of a large capacity secondary cache using SSDs
Enables tiering between DRAM cache and SSDs (secondary cache)
Most reads are served directly from high performance tiered cache
Benefits
  Enhances performance during peak workload
  Non-disruptive and transparent to applications
DRAM Cache
SSD
Tiered Cache
Tier 0
Storage system
Tier 1
Notes: Tiering is also implemented at the cache level. A large cache in a storage system improves performance by retaining large amount of frequently accessed data in a cache; so most reads are served directly from the cache. However, configuring a large cache in the storage system involves more cost. An alternative way to increase the size of the cache is by utilizing the SSDs on the storage system. In cache tiering, SSDs are used to create a large capacity secondary cache and to enable tiering between DRAM (primary cache) and SSDs (secondary cache). Server flash-caching is another tier of cache in which flash-cache card is installed in the server to further enhance the application performance.

## Slide 27: Server Flash-caching Technology
Uses intelligent caching software and PCIe flash card on compute system
Dramatically improves application performance
  Provides performance acceleration for read-intensive workloads
  Avoids network latencies associated with I/O access to the storage system
Intelligently determines data that would benefit by sitting in compute system on PCIe flash
Uses minimal CPU and memory resources
  Flash management is offloaded onto PCIe card
PCIe Flash
Card
HBA
Application
Intelligent Caching Software
Compute System
Storage
Network
Storage System
Notes: Server flash-caching technology uses intelligent caching software and a PCI Express-based (PCIe) flash card installed on the compute system. This dramatically improves application performance by reducing latency, and accelerates throughput. Server flash-caching technology works in both physical and virtual environments and provides performance acceleration for read-intensive workloads. This technology uses minimal CPU and memory resources from the compute system by offloading flash management onto the PCIe card.
It intelligently determines which data would benefit by sitting in the compute system on PCIe flash and closer to the application. This avoids the latencies associated with I/O access over the network to the storage system. With this, the processing power required for an application’s most frequently referenced data is offloaded from the back-end storage to the PCIe card. Therefore, the storage system can allocate greater processing power to other applications.

## Slide 28: Use Case – Block-based Storage in Cloud
Storage as a Service
Block-based storage volumes
Block-based storage system
VM instances running business applications
Notes: To gain cost advantage, organizations may move their application to cloud. To ensure proper functioning of the application and provide acceptable performance, service providers offer block-based storage in cloud. The service providers enable the consumers to create a block-based storage volumes and attach them to the virtual machine instances. After the volumes are attached, the consumers can create the file system on these volumes and run applications the way they would on an on-premise data center.

## Slide 29: Lesson 3: Summary
During this lesson the following topics were covered:
LUN and Sub-LUN tiering
Cache tiering
Server flash caching
Block-based storage use case
Notes: This lesson covered LUN and Sub-LUN tiering, cache tiering, server flash caching, and block-based storage use case.

## Slide 30: Module 3: Summary
Key points covered in this module:
Components of block-based storage system
Traditional and virtual storage provisioning
Storage tiering mechanisms
Notes: This module covered various components of block-based storage system. This module also covered traditional and virtual storage provisioning methods. Finally, this module covered storage tiering mechanisms.

## Slide 31: What is IP SAN?
A SAN that uses Internet Protocol (IP) for the transport of block-level data
Uses IP-based protocols for communication, commonly:
  Internet SCSI (iSCSI)
  Fibre Channel over IP (FCIP)
Notes: IP SAN uses Internet Protocol (IP) for the transport of storage traffic. It transports block I/O over an IP-based network. Two primary protocols that leverage IP as the transport mechanism for block-level data transmission are Internet SCSI (iSCSI) and Fibre Channel over IP (FCIP). These protocols are covered in this module.

## Slide 32: Drivers for IP SAN
Existing IP-based network infrastructure can be leveraged
  Reduced cost compared to deploying new FC SAN infrastructure
IP network makes it possible to extend or connect SANs over long distances
Many long-distance disaster recovery solutions already leverage IP-based network
Many robust and mature security options are available for IP network
Notes: Fibre Channel (FC) SAN provides high performance and scalability. These advantages of FC SAN come with the additional cost of buying FC components, such as FC HBA and FC switches. IP is a matured technology and using IP as a storage networking option provides several advantages. These are listed below:
Most organizations have an existing IP-based network infrastructure, which could also be used for storage networking and may be a more economical option than deploying a new FC SAN infrastructure.
IP network has no distance limitation, which makes it possible to extend or connect SANs over long distances. With IP SAN, organizations can extend the geographical reach of their storage infrastructure and transfer data that are distributed over wide locations.
Many long-distance disaster recovery (DR) solutions are already leveraging IP-based networks. In addition, many robust and mature security options are available for IP networks.

## Slide 33: Lesson 1: iSCSI
This lesson covers the following topics:
iSCSI network components
iSCSI connectivity
iSCSI protocol stack
iSCSI address and name
iSCSI discovery
Notes: This lesson covers iSCSI network components and connectivity. It also covers iSCSI protocol stack, iSCSI address and name, and iSCSI discovery.

## Slide 34: iSCSI Overview
IP-based protocol that enables transporting SCSI data over an IP network
Encapsulates SCSI I/O into IP packets and transports them using TCP/IP
Notes: iSCSI is an IP-based protocol that establishes and manages connections between compute systems and storage systems over IP. iSCSI is an encapsulation of SCSI I/O over IP. iSCSI encapsulates SCSI commands and data into IP packets and transports them using TCP/IP. iSCSI is widely adopted for transferring SCSI data over IP between compute systems and storage systems and among the storage systems. It is relatively inexpensive and easy to implement, especially environments in which an FC SAN does not exist.

## Slide 35: Components of iSCSI Network
iSCSI initiators
  Example: iSCSI HBA
iSCSI targets
  Example: Storage system with iSCSI port
IP-based network
  Example: Gigabit Ethernet LAN
Compute Systems
IP
Storage Systems
iSCSI Port
iSCSI HBA
Notes: Key components for iSCSI communication are:
iSCSI initiators such as an iSCSI HBA
iSCSI targets such as a storage system with an iSCSI port
IP-based network such as a Gigabit Ethernet LAN
An iSCSI initiator sends commands and associated data to a target and the target returns data and responses to the initiator.

## Slide 36: Types of iSCSI Initiator
Standard NIC with software iSCSI adapter
  NIC provides network interface
  Software adapters provide iSCSI functionality
  Both iSCSI and TCP/IP processing require CPU cycles of compute system
TCP Offload Engine (TOE) NIC with software iSCSI adapter
  TOE NIC performs TCP/IP processing
  Software adapter provides iSCSI functionality
  iSCSI processing requires CPU cycles of compute system
iSCSI HBA
  Performs both iSCSI and TCP/IP processing
  Frees-up CPU cycles of compute system for business applications
Notes: A standard NIC with software iSCSI adapter, a TCP offload engine (TOE) NIC with software iSCSI adapter, and an iSCSI HBA are the three common types of iSCSI initiators. These initiators are described below:
Standard NIC with software iSCSI adapter: The software iSCSI adapter is an operating system (OS) or hypervisor kernel-resident software that uses an existing NIC of the compute system to emulate an iSCSI initiator. It is least expensive and easy to implement because most compute systems come with at least one, and in many cases two embedded NICs. It requires only a software initiator for iSCSI functionality. Because NICs provide standard networking function, both the TCP/IP processing and the encapsulation of SCSI data into IP packets are carried out by the CPU of the compute system. This places additional overhead on the CPU. If a standard NIC is used in heavy I/O load situations, the CPU of the compute system might become a bottleneck.
TOE NIC with software iSCSI adapter: A TOE NIC offloads the TCP/IP processing from the CPU of a compute system and leaves only the iSCSI functionality to the CPU. The compute system passes the iSCSI information to the TOE NIC and then the TOE NIC sends the information to the destination using TCP/IP. Although this solution improves performance, the iSCSI functionality is still handled by a software adapter that requires CPU cycles of the compute system.
iSCSI HBA: An iSCSI HBA is a hardware adapter with built-in iSCSI functionality. It is capable of providing performance benefits over software iSCSI adapters by offloading the entire iSCSI and TCP/IP processing from the CPU of a compute system.

## Slide 37: iSCSI Connectivity
Native
  iSCSI initiators connect to iSCSI targets directly/through IP network
  No FC component
Bridged
  iSCSI initiators are attached to IP network
  Storage systems are attached to FC SAN
  iSCSI gateway provides bridging functionality
Compute System
iSCSI HBA
IP
Storage System
iSCSI Port
Compute System
iSCSI HBA
IP
Storage System
FC Port
FC SAN
iSCSI
Gateway
Native iSCSI
Bridged iSCSI
Notes: The iSCSI implementations support two types of connectivity: native and bridged. These are described below:
Native iSCSI: In this type of connectivity, the compute systems with iSCSI initiators may be either directly attached to the iSCSI targets (iSCSI-capable storage systems) or connected through an IP-based network. FC components are not required for native iSCSI connectivity. The figure on the left shows a native iSCSI implementation that includes a storage system with an iSCSI port. The storage system is connected to an IP network. After an iSCSI initiator is logged on to the network, it can access the available LUNs on the storage system.
Bridged iSCSI: This type of connectivity allows the initiators to exist in an IP environment while the storage systems remain in an FC SAN environment. It enables the coexistence of FC with IP by providing iSCSI-to-FC bridging functionality. The figure on the right illustrates a bridged iSCSI implementation. It shows connectivity between a compute system with an iSCSI initiator and a storage system with an FC port. As the storage system does not have any iSCSI port, a gateway or a multiprotocol router is used. The gateway facilitates the communication between the compute system with iSCSI ports and the storage system with only FC ports. The gateway converts IP packets to FC frames and vice versa, thereby bridging the connectivity between the IP and FC environments. The gateway contains both FC and Ethernet ports to facilitate the communication between the FC and the IP environments. The iSCSI initiator is configured with the gateway’s IP address as its target destination. On the other side, the gateway is configured as an FC initiator to the storage system.

## Slide 38: Combining FC and Native iSCSI Connectivity
Storage system provides both FC and iSCSI ports
  Enable iSCSI and FC connectivity in the same environment
  No bridge device is needed
FC HBA
Compute System
iSCSI HBA
Storage System
FC Port
iSCSI Port
Compute System
IP
FC SAN
Notes: Typically, a storage system comes with both FC and iSCSI ports. This enables both the native iSCSI connectivity and the FC connectivity in the same environment, as shown on the slide.

## Slide 39: iSCSI Protocol Stack
Ethernet
IP
TCP
iSCSI
SCSI
Data
OSI Model
iSCSI Initiator
iSCSI Target
Layer 7 Application
Layer 5 Session
Layer 4 Transport
Layer 3 Network
Layer 2 Data Link
SCSI
iSCSI
TCP
IP
Ethernet
SCSI
iSCSI
TCP
IP
Ethernet
Interconnect
Commands and Data
Login and Discovery
Windows and Segments
Packets
Frames
Notes: The figure on the slide displays a model of iSCSI protocol layers and depicts the encapsulation order of the SCSI commands for their delivery through a physical carrier.
SCSI is the command protocol that works at the application layer of the Open System Interconnection (OSI) model. The initiators and the targets use SCSI commands and responses to talk to each other. The SCSI commands, data, and status messages are encapsulated into TCP/IP and transmitted across the network between the initiators and the targets.
iSCSI is the session-layer protocol that initiates a reliable session between devices that recognize SCSI commands and TCP/IP. The iSCSI session-layer interface is responsible for handling login, authentication, target discovery, and session management.
TCP is used with iSCSI at the transport layer to provide reliable transmission. TCP controls message flow, windowing, error recovery, and retransmission. It relies upon the network layer of the OSI model to provide global addressing and connectivity. The OSI Layer 2 protocols at the data link layer of this model enable node-to-node communication through a physical network.

## Slide 40: iSCSI Address and Name
iSCSI address is the path to iSCSI initiator/target, which is comprised of:
  Location of iSCSI initiator/target
    Combination of IP address and TCP port number
  iSCSI name
    Unique identifier for initiator/target in an iSCSI network
IQN: iSCSI Qualified Name
  iqn.2008-02.com.example:optional_string
EUI: Extended Unique Identifier
  eui.0300732A32598D26
NAA: Network Address Authority
  naa.52004567BA64678D
Common Types of iSCSI Name
Notes: Both the initiators and the targets in an iSCSI environment have iSCSI addresses that facilitate communication between them. An iSCSI address is comprised of the location of an iSCSI initiator or target on the network and the iSCSI name. The location is a combination of the host name or IP address and the TCP port number. For iSCSI initiators, the TCP port number is omitted from the address.
iSCSI name is a unique worldwide iSCSI identifier that is used to identify the initiators and targets within an iSCSI network to facilitate communication. The unique identifier can be a combination of the names of the department, application, manufacturer, serial number, asset number, or any tag that can be used to recognize and manage the iSCSI nodes. The following are three types of iSCSI names commonly used:
  iSCSI Qualified Name (IQN): An organization must own a registered domain name to generate iSCSI Qualified Names. This domain name does not need to be active or resolve to an address. It just needs to be reserved to prevent other organizations from using the same domain name to generate iSCSI names. A date is included in the name to avoid potential conflicts caused by the transfer of domain names. An example of an IQN is iqn.2015-04.com.example:optional_string. The optional_string provides a serial number, an asset number, or any other device identifiers. IQN enables storage administrators to assign meaningful names to the iSCSI initiators and the iSCSI targets, and therefore, manages those devices more easily.
  Extended Unique Identifier (EUI): An EUI is a globally unique identifier based on the IEEE EUI-64 naming standard. An EUI is composed of the eui prefix followed by a 16-character hexadecimal name, such as eui.0300732A32598D26.
  Network Address Authority (NAA): NAA is another worldwide unique naming format as defined by the InterNational Committee for Information Technology Standards (INCITS) T11 - Fibre Channel (FC) protocols and is used by Serial Attached SCSI (SAS). This format enables the SCSI storage devices that contain both iSCSI ports and SAS ports to use the same NAA-based SCSI device name. An NAA is composed of the naa prefix followed by a hexadecimal name, such as naa.52004567BA64678D. The hexadecimal representation has a maximum size of 32 characters (128 bit identifier).

## Slide 41: iSCSI Discovery
For iSCSI communication, initiator must discover location and name of targets on the network
iSCSI discovery commonly takes place in two ways:
  SendTargets discovery
    Initiator is manually configured with the target’s network portal
    Initiator issues SendTargets command; target responds with required parameters
  Internet Storage Name Service (iSNS)
    Initiators and targets register themselves with iSNS server
    Initiator may query iSNS server for a list of available targets
Notes: An iSCSI initiator must discover the location of its targets on the network and the names of the targets available to it before it can establish a session. This discovery commonly takes place in two ways: SendTargets discovery or internet Storage Name Service (iSNS).
SendTargets discovery: In SendTargets discovery, the initiator is manually configured with the target’s network portal (IP address and TCP port number) to establish a discovery session. The initiator issues the SendTargets command, and thereby the target network portal responds to the initiator with the location and name of the target.
iSNS: iSNS in the iSCSI SAN is equivalent in function to the Name Server in an FC SAN. It enables automatic discovery of iSCSI devices on an IP-based network. The initiators and targets can be configured to automatically register themselves with the iSNS server. Whenever an initiator wants to know the targets that it can access, it can query the iSNS server for a list of available targets.

## Slide 42: iSNS Discovery Domain
iSNS
iSCSI Initiators
iSCSI Target
iSCSI Target
iSCSI Initiator
Discovery Domains
Queries and Notifications
Notes: iSNS discovery domains function in the same way as FC zones. Discovery domains provide functional groupings of devices (including iSCSI initiators and targets) in an IP SAN. The iSNS server is configured with discovery domains. For devices to communicate with one another, they must be configured in the same discovery domain.
The iSNS server may send state change notifications (SCNs) to the registered devices. State change notifications (SCNs) inform the registered devices about network events that affect the operational state of devices such as the addition or removal of devices from a discovery domain.

## Slide 43: Lesson 1: Summary
During this lesson the following topics were covered:
iSCSI network components
iSCSI connectivity
iSCSI protocol stack
iSCSI address and name
iSCSI discovery
Notes: This lesson covered the iSCSI network components and connectivity. It also covered iSCSI protocol stack, iSCSI address and name, and iSCSI discovery methods.

## Slide 44: Lesson 2: Link Aggregation and VLAN
This lesson covers the following topics:
Link aggregation
Switch aggregation
Self-forming network
Virtual LAN (VLAN)
Stretched VLAN
Notes: This lesson covers link aggregation, switch aggregation, and self-forming network. It also covers virtual LAN (VLAN) and stretched VLAN.

## Slide 45: Link and Switch Aggregation
Link aggregation:
  Distributes network traffic across aggregated links
  Provides higher throughput than a single link could provide
Switch aggregation:
  Aggregated physical switches appear as a single logical switch
  Distributes traffic across all links from aggregated switches
  Provides higher throughput than a single switch could provide
Switch Aggregation
Ethernet Director
Aggregated Links
Ethernet Switch
Compute Systems
Aggregated Links
Ethernet Switch
Storage System
Aggregated Links
Ethernet Switch
Compute Systems
Ethernet Switch
Storage System
Notes: Like an FC environment, the link aggregation in an Ethernet network also combines two or more parallel network links into a single logical link (port-channel). Link aggregation enables obtaining higher throughput than a single link could provide. It also enables distribution of network traffic across the links that ensure even link utilization. If a link in the aggregation is lost, all network traffic on that link is redistributed across the remaining links. Link aggregation can be performed for links between two switches and between a switch and a node. The figure on the left shows an example of link aggregation between two Ethernet switches. In this example, four links between the switches are aggregated into a single port-channel.
Switch aggregation combines two physical switches to make them appear as a single logical switch. All network links from these physical switches appear as a single logical link. This enables nodes to use a port-channel across two switches. The network traffic is also distributed across all the links in the port-channel. Switch aggregation allows ports in both the switches to be active and to forward network traffic simultaneously. Therefore, it provides more active paths and throughput than a single switch or multiple non-aggregated switches under normal conditions, resulting in improved node performance. With switch aggregation, if one switch in the aggregation fails, network traffic will continue to flow through another switch. The figure on the right shows an example of switch aggregation. In this example, four physical links to the aggregated switches appear as a single logical link to the third switch.

## Slide 46: Self-forming Network and Link Aggregation
Self-forming network:
  Allows an Ethernet switch to join an Ethernet network automatically
  Network automatically detects new switch, discovers topology, and populate routing table to start forwarding traffic immediately
Self-forming link aggregation:
  Includes new interswitch links into a port-channel automatically and redistributes network traffic among all aggregated links
Simplify configuration and ongoing management operations
Reduce manual, repetitive, and error-prone configuration tasks
Provide agility needed to deploy, scale, and manage network infrastructure
Benefits
Notes: Self-forming network allows an Ethernet switch to join an Ethernet network automatically. To join an Ethernet network, the new switch is simply powered-up and cabled to an existing switch in the network. The Ethernet network automatically detects the new switch and populates its routing table to start forwarding network traffic immediately.
Self-forming link aggregation enables an Ethernet network to automatically include new interswitch links into a port-channel and redistributes network traffic among all the links in the port-channel. Instead of manually configuring individual links into a port-channel on multiple Ethernet switches, port-channels are automatically formed when new connections (links) are added between the switches. This enables an organization to scale network bandwidth between the Ethernet switches quickly.
Both the self-forming network and the self-forming link aggregation help in meeting the third platform requirements. They simplify the configuration and ongoing management operations of network infrastructures by automating some of the configuration tasks. They also reduce manual, repetitive, and error-prone network configuration tasks. Further, they provide the agility needed to deploy, scale, and manage the network infrastructure.

## Slide 47: Virtual LAN (VLAN)
Helps isolating iSCSI traffic from other network traffic in a physical Ethernet network
Configuring a VLAN:
  Define VLANs on switches with specific VLAN IDs
  Configure VLAN membership based on a supported technique
    Port-based, MAC-based, protocol-based, IP subnet address-based, or application-based
A logical network created on a LAN enabling communication between a group of nodes with a common set of functional requirements, independent of their physical location in the network.
VLAN
Notes: Virtual LANs (VLANs) are logical networks created on a LAN. A VLAN enables communication between a group of nodes (compute systems and storage systems) with a common set of functional requirements independent of their physical location in the network. VLANs are particularly well-suited for iSCSI deployments as they enable isolating the iSCSI traffic from other network traffic (for example, compute-to-compute traffic) when a physical Ethernet network is used to transfer different types of network traffic.
A VLAN conceptually functions in the same way as a VSAN. Each VLAN behaves and is managed as an independent LAN. Two nodes connected to a VLAN can communicate between themselves without routing of frames – even if they are in different physical locations. VLAN traffic must be forwarded via a router or OSI Layer-3 switching device when two nodes in different VLANs are communicating – even if they are connected to the same physical LAN. Network broadcasts within a VLAN generally do not propagate to nodes that belong to a different VLAN, unless configured to cross a VLAN boundary.
To configure VLANs, an administrator first defines the VLANs on the switches. Each VLAN is identified by a unique 12-bit VLAN ID (as per IEEE 802.1Q standard). The next step is to configure the VLAN membership based on an appropriate technique supported by the switches, such as port-based, MAC-based, protocol-based, IP subnet address-based, and application-based. In the port-based technique, membership in a VLAN is defined by assigning a VLAN ID to a switch port. When a node connects to a switch port that belongs to a VLAN, the node becomes a member of that VLAN. In the MAC-based technique, the membership in a VLAN is defined on the basis of the MAC address of the node. In the protocol-based technique, different VLANs are assigned to different protocols based on the protocol type field found in the OSI Layer 2 header. In the IP subnet address-based technique, the VLAN membership is based on the IP subnet address. All the nodes in an IP subnet are members of the same VLAN. In the application-based technique, a specific application, for example, a file transfer protocol (FTP) application can be configured to execute on one VLAN. A detailed discussion on these VLAN configuration techniques is beyond the scope of this course.

## Slide 48: VLAN Trunking and Tagging
VLAN trunking allows a single network link (trunk link) to carry multiple VLAN traffic
To enable trunking, trunk ports must be configured on both sending and receiving network components
Sending network component inserts a tag field containing VLAN ID into an Ethernet frame before sending through a trunk link
Receiving network component reads the tag and forwards the frame to destination port(s)
  Tag is removed once a frame leaves trunk link to reach a node port
Notes: Similar to the VSAN trunking, network traffic from multiple VLANs may traverse a trunk link. A single network port, called trunk port, is used for sending or receiving traffic from multiple VLANs over a trunk link. Both the sending and the receiving network components must have at least one trunk port configured for all or a subset of the VLANs defined on the network component.
As with VSAN tagging, VLAN has its own tagging mechanism. The tagging is performed by inserting a 4-byte tag field containing 12-bit VLAN ID into the Ethernet frame (as per IEEE 802.1Q standard) before it is transmitted through a trunk link. The receiving network component reads the tag and forwards the frame to the destination port(s) that corresponds to that VLAN ID. The tag is removed once the frame leaves a trunk link to reach a node port.
Note: IEEE 802.1ad Multi-tagging
IEEE 802.1ad is an amendment to IEEE 802.1Q and enables inserting multiple VLAN tags to an Ethernet frame. IEEE 802.1Q mandates a single tag with a 12-bit VLAN ID field, which limits the number of VLANs in an environment theoretically up to 4096. In a large environment such as a cloud infrastructure, this limitation may restrict VLAN scalability. IEEE 802.1ad provides the flexibility to accommodate a larger number of VLANs. For example, by using a double-tag, theoretically 16777216 (4096×4096 ) VLANs may be configured.

## Slide 49: Stretched VLAN
WAN
VLAN 10 and 20 Traffic
Storage System
Storage System
Compute Systems
VLAN 20
VLAN 10
Compute Systems
Site 1
Ethernet
Switch
Ethernet
Director
VLAN 10
VLAN 20
Storage System
Storage System
Compute Systems
VLAN 20
VLAN 10
Compute Systems
Site 2
Ethernet
Switch
Ethernet
Director
VLAN 10
VLAN 20
A VLAN that spans multiple sites and enables OSI Layer 2 communication between a group of nodes over an OSI Layer 3 WAN infrastructure, independent of their physical location.
Stretched VLAN
Notes: A stretched VLAN is a VLAN that spans across multiple sites over a WAN connection. In a typical multi-site environment, network traffic between sites is routed through an OSI Layer 3 WAN connection. Because of the routing, it is not possible to transmit OSI Layer 2 traffic between the nodes in two sites. A stretched VLAN extends a VLAN across the sites and enables nodes in two different sites to communicate over a WAN as if they are connected to the same network.
Stretched VLANs also allow the movement of virtual machines (VMs) between sites without the need to change their network configurations. This simplifies the creation of high-availability clusters, VM migration, and application and workload mobility across sites. The clustering across sites, for example, enables moving VMs to an alternate site in the event of a disaster or during the maintenance of one site. Without a stretched VLAN, the IP addresses of the VMs must be changed to match the addressing scheme at the other site.

## Slide 50: Lesson 2: Summary
During this lesson the following topics were covered:
Link aggregation
Switch aggregation
Self-forming network
VLAN configuration, trunking, and tagging
Stretched VLAN
Notes: This lesson covered link aggregation, switch aggregation, and self-forming network. It also covered VLAN configuration, VLAN trunking, VLAN tagging, and stretched VLAN.

## Slide 51: Module 4: Summary
Key points covered in this module:
iSCSI protocol, network components, and connectivity
Link aggregation, switch aggregation, and VLAN
Notes: This module covered IP SAN protocols such as iSCSI and FCIP, components, and connectivity. It also covered link aggregation, switch aggregation, and VLAN.

## Slide 52: Lesson 1: Overview of FCoE SAN
This lesson covers the following topics:
Components of FCoE SAN
FCoE SAN connectivity
VLAN and VSAN in FCoE
FCoE port types
Notes: This lesson covers the components of an FCoE SAN, FCoE SAN connectivity, VLAN and VSAN in FCoE, and FCoE port types.

## Slide 53: What is FCoE SAN?
A SAN that transports FC data along with regular Ethernet traffic over a Converged Enhanced Ethernet (CEE) network
Uses FCoE protocol that encapsulates FC frames into Ethernet frames
Ensures lossless transmission of FC traffic over Ethernet
Notes: FCoE SAN is a Converged Enhanced Ethernet (CEE) network that is capable of transporting FC data along with regular Ethernet traffic over high speed (such as 10 Gbps or higher) Ethernet links. It uses FCoE protocol that encapsulates FC frames into Ethernet frames. FCoE protocol is defined by the T11 standards committee. FCoE is based on an enhanced Ethernet standard that supports Data Center Bridging (DCB) functionalities (also called CEE functionalities). DCB ensures lossless transmission of FC traffic over Ethernet. The DCB functionalities are covered later in this module.

## Slide 54: Drivers for FCoE SAN
Multi-function network components are used to transfer both compute-to-compute and FC storage traffic
  Reduces the complexity of managing multiple discrete networks
  Reduces the number of network adapters, cables, and switches required in a data center
  Reduces power and space consumption in a data center
Notes: Data centers typically have multiple networks to handle various types of network traffic – for example, an Ethernet LAN for TCP/IP communication and an FC SAN for FC communication. TCP/IP is typically used for compute-to-compute communication, data backup, infrastructure management communication, and so on. FC is typically used for moving block-level data between storage systems and compute systems. To support multiple networks, compute systems in a data center are equipped with multiple redundant physical network interfaces – for example, multiple Ethernet and FC network adapters. In addition, to enable the communication, different types of networking switches and physical cabling infrastructure are implemented in data centers. The need for two different kinds of physical network infrastructure increases the overall cost and complexity of data center operation.
FCoE SAN provides the flexibility to deploy the same network components for transferring both compute-to-compute traffic and FC storage traffic. This helps to mitigate the complexity of managing multiple discrete network infrastructures. FCoE SAN uses multi-functional network adapters and switches. Therefore, FCoE reduces the number of network adapters, cables, and switches, along with power and space consumption required in a data center.

## Slide 55: Components of FCoE SAN
Network adapters
  Example: Converged Network Adapter (CNA) and software FCoE adapter
Cables
  Example: Copper cables and fiber optical cables
FCoE switch
Compute Systems
Storage Systems
FC Port
CNA
LAN
FC SAN
FCoE Switch
CEE Link
Notes: The key FCoE SAN components are:
Network adapters such as Converged Network Adapter (CNA) and software FCoE adapter
Cables such as copper cables and fiber optical cables
FCoE switch
The CNA, software FCoE adapter, and FCoE switch are detailed in the following slides.

## Slide 56: CNA and Software FCoE Adapter
CNA:
  A physical adapter that provides functionality of both NIC and FC HBA
  Encapsulates FC frames into Ethernet frames and forwards them over CEE links
  Contains separate modules for 10 GE, FC, and FCoE ASICs
Software FCoE adapter:
  An OS/hypervisor-resident software that performs FCoE processing
  Supported NICs transfer both FCoE traffic and regular Ethernet traffic
Notes: The CNA is a physical adapter that provides the functionality of both a standard NIC and an FC HBA in a single device. It consolidates both FC traffic and regular Ethernet traffic on a common Ethernet infrastructure. CNAs connect compute systems to the FCoE switches. They are responsible for encapsulating FC traffic onto Ethernet frames and forwarding them to FCoE switches over CEE links. They eliminate the need to deploy separate adapters and cables for FC and Ethernet communications, thereby reducing the required number of network adapters and switch ports. A CNA offloads the FCoE protocol processing task from the compute system, thereby freeing the CPU resources of the compute system for application processing. It contains separate modules for 10 Gigabit Ethernet (GE), FC, and FCoE Application Specific Integrated Circuits (ASICs). The FCoE ASIC encapsulates FC frames into Ethernet frames. One end of this ASIC is connected to 10 GE and FC ASICs for compute system connectivity, while the other end provides a 10 GE interface to connect to an FCoE switch.
Instead of a CNA, a software FCoE adapter may also be used. A software FCoE adapter is OS or hypervisor kernel-resident software that performs FCoE processing. The FCoE processing consumes compute system CPU cycles. With software FCoE adapters, the OS or hypervisor implements FC protocol in software that handles SCSI to FC processing. The software FCoE adapter performs FC to Ethernet encapsulation. Both FCoE traffic (Ethernet traffic that carries FC data) and regular Ethernet traffic are transferred through supported NICs on the compute system.

## Slide 57: FCoE Switch
Provides both Ethernet switch and FC switch functionalities
Consists of FCF, Ethernet bridge, and ports for FC and Ethernet connectivity
  FCF functions as the communication bridge between CEE and FC networks
    Handles FCoE login requests, applies zoning, and provides fabric services
    Encapsulates and decapsulates FC frames
Forwards frames based on Ethertype
FC Port
Fibre Channel Forwarder (FCF)
FC Port
FC Port
FC Port
Ethernet
Port
Ethernet
Port
Ethernet
Port
Ethernet
Port
Ethernet Bridge
Notes: An FCoE switch has both Ethernet switch and FC switch functionalities. It has a Fibre Channel Forwarder (FCF), an Ethernet Bridge, and a set of ports that can be used for FC and Ethernet connectivity. FCF handles FCoE login requests, applies zoning, and provides the fabric services typically associated with an FC switch. It also encapsulates the FC frames received from the FC port into the Ethernet frames and decapsulates the Ethernet frames received from the Ethernet Bridge to the FC frames.
Upon receiving the incoming Ethernet traffic, the FCoE switch inspects the Ethertype (used to indicate which protocol is encapsulated in the payload of an Ethernet frame) of the incoming frames and uses that to determine their destination. If the Ethertype of the frame is FCoE, the switch recognizes that the frame contains an FC payload and then forwards it to the FCF. From there, the FC frame is extracted from the Ethernet frame and transmitted to the FC SAN over the FC ports. If the Ethertype is not FCoE, the switch handles the traffic as usual Ethernet traffic and forwards it over the Ethernet ports.

## Slide 58: FCoE SAN Connectivity
FCoE switches interconnect a CEE network containing compute systems with an FC SAN containing storage systems
  Suitable for environment with existing FC SAN
FCoE with Existing FC SAN
Compute
Systems
with CNA
FCoE Port
LAN
FC SAN
Storage System
FC Ports
FCoE Switch
FCoE Switch
FCoE Port
Notes: The most common FCoE connectivity uses FCoE switches to interconnect a CEE network containing compute systems with an FC SAN containing storage systems. The compute systems have FCoE ports that provide connectivity to the FCoE switches. The FCoE switches enable the consolidation of FC traffic and Ethernet traffic onto CEE links.
This type of FCoE connectivity is suitable when an organization has an existing FC SAN environment. Connecting FCoE compute systems to the FC storage systems through FCoE switches do not require any change in the FC environment.

## Slide 59: FCoE SAN Connectivity
FCoE switches interconnect FCoE compute systems with FCoE storage systems
  Suitable for new FCoE deployments
End-to-end FCoE
Compute
Systems
with CNA
LAN
FC SAN
Storage System
FCoE Ports
FCoE Switch
FCoE Switch
FCoE Switch
FCoE Switch
FCoE Port
FCoE Port
Notes: Some vendors offer FCoE ports in their storage systems. These storage systems connect directly to the FCoE switches. The FCoE switches form FCoE fabrics between compute systems and storage systems and provide end-to-end FCoE support. The end-to-end FCoE connectivity is suitable for a new FCoE deployment.

## Slide 60: VLAN and VSAN in FCoE
Both VLAN and VSAN may exist in the FCoE with existing FC SAN environment
FCoE switch supports VSAN to VLAN mapping
A dedicated VLAN is configured for each VSAN
VLANs configured for VSANs should not carry regular LAN traffic
Compute System with CNA
Trunk Link for VLAN 10,20,30,40
Trunk Link for VLAN 10,20
Trunk Link for VSAN 100,200
Ethernet Switch
FCoE Switch
FC Switch
Storage Systems
VLAN | VSAN | FCoE
10 | N/A | No
20 | N/A | No
30 | 100 | Yes
40 | 200 | Yes
VSAN
100
200
VLAN
10
20
Notes: FCoE protocol enables transmission of FC SAN traffic through an Ethernet LAN that supports Data Center Bridging (DCB) functionalities. If VLANs and VSANs are created on the LAN and FC SAN respectively, a mapping is required between the VLANs and VSANs. The mapping determines which VLAN will carry FC traffic that belongs to a VSAN. The VSAN to VLAN mapping is performed at the FCoE switch. Multiple VSANs are not allowed to share a VLAN; hence a dedicated VLAN must be configured at the FCoE switch for each VSAN. It is also recommended that VLANs that carry regular LAN traffic should not be used for VSAN traffic.
The figure on the slide provides an example of mapping between VLANs and VSANs. In this example, the FCoE switch is configured with four VLANs – VLAN 10, VLAN 20, VLAN 30, and VLAN 40. The Ethernet switch is configured with two VLANs – VLAN 10 and VLAN 20. Both VLAN 10 and VLAN 20 transfer regular LAN traffic to enable compute-to-compute communication. The FC switch has VSAN 100 and VSAN 200 configured. To allow data transfer between the FCoE compute system and the FC storage systems through the FCoE switch, VSAN 100 and VSAN 200 must be mapped to VLANs configured on the FCoE switch. As VLAN 10 and VLAN 20 are already being used for regular LAN traffic, VSAN 100 and VSAN 200 should be mapped to VLAN 30 and VLAN 40 respectively.

## Slide 61: Port Types in FCoE
VN_Port
FCoE
Switch
VF_Port
FC Switch
FCoE
Storage
System
N_Port
F_Port
E_Port
E_Port
Compute System
VN_Port
VF_Port
ISL
VE_Port
VE_Port
Compute System
FCoE Switch
VN_Port
ISL
VF_Port
FC
Storage
System
Notes: FCoE utilizes virtual ports, which emulate the behavior of regular FC ports. FCoE virtual ports establish virtual FC links between the devices in an FCoE SAN. The different FCoE port types are listed below:
VN_Port: It is an end point in an FCoE SAN. Typically, it is a CNA port or an FCoE storage system port that is connected to an FCoE switch in the FCoE SAN.
VF_Port: It is a port on an FCoE switch that connects a VN_Port.
VE_Port: It is a port that forms the connection between two FCoE switches. The VE_Port on an FCoE switch connects to the VE_Ports of another FCoE switch in an FCoE SAN.

## Slide 62: Lesson 1: Summary
During this lesson the following topics were covered:
Components of FCoE SAN
FCoE SAN connectivity
VLAN and VSAN in FCoE
FCoE port types
Notes: This lesson covered the components of an FCoE SAN, FCoE SAN connectivity, VLAN and VSAN in FCoE, and FCoE port types.

## Slide 63: Lesson 2: Converged Enhanced Ethernet (CEE)
This lesson covers the following topics:
Priority-based flow control
Enhanced transmission selection
Congestion notification
Data center bridging exchange protocol
Notes: This lesson covers Converged Enhanced Ethernet (CEE) and its functionalities – priority-based flow control, enhanced transmission selection, congestion notification, and data center bridging exchange protocol.

## Slide 64: Introduction to CEE
CEE refers to a set of enhancements to conventional Ethernet for making it lossless and for converging various traffic types
CEE ensures lossless transmission of FC data over an Ethernet network
  Eliminates the dropping of frames due to congestion
CEE requires these functionalities:
  Priority-based flow control (PFC)
  Enhanced transmission selection (ETS)
  Congestion notification (CN)
  Data center bridging exchange protocol (DCBX)
Notes: Conventional Ethernet is lossy in nature, which means that frames might be dropped or lost under congestion conditions. Converged Enhanced Ethernet (CEE) provides a new specification to the existing Ethernet standard. It eliminates the lossy nature of Ethernet and enables convergence of various types of network traffic on a common Ethernet infrastructure. CEE eliminates the dropping of frames due to congestion and thereby ensures lossless transmission of FCoE traffic over an Ethernet network.
The lossless Ethernet is required for the reliable transmission of FC data over an Ethernet network. Unlike TCP/IP, the loss of a single FC frame typically requires the entire FC exchange to be aborted and re‐transmitted, instead of just re‐sending a particular missing frame. CEE makes a high-speed (such as 10 Gbps or higher) Ethernet network a viable storage networking option, similar to an FC SAN.
The CEE requires certain functionalities. These functionalities are defined and maintained by the data center bridging (DCB) task group, which is a part of the IEEE 802.1 working group. These functionalities are:
  Priority-based flow control
  Enhanced transmission selection
  Congestion notification
  Data center bridging exchange protocol
Each of these functionalities is described in the following slides.

## Slide 65: Priority-based Flow Control (PFC)
Creates eight virtual links on a single physical link
Uses PAUSE capability of Ethernet for each virtual link
  A virtual link can be paused and restarted independently
  PAUSE mechanism is based on user priorities or classes of service
Notes: Traditional FC manages congestion through the use of a link-level, credit-based flow control that guarantees no loss of FC frames. Typical Ethernet, coupled with TCP/IP, uses a packet drop flow control mechanism. The packet drop flow control is not lossless. This challenge is eliminated by using an IEEE 802.3x Ethernet PAUSE control frame to create a lossless Ethernet. A receiver can send a PAUSE request to a sender when the receiver’s buffer is filling up. Upon receiving a PAUSE frame, the sender stops transmitting frames, which guarantees no loss of frames. The downside of using the Ethernet PAUSE frame is that it operates on the entire link, which might be carrying multiple traffic flows.
PFC provides a link-level flow control mechanism. PFC creates eight separate virtual links on a single physical link and allows any of these links to be paused and restarted independently. PFC enables the PAUSE mechanism based on user priorities or classes of service. Enabling the PAUSE based on priority allows creating lossless links for network traffic, such as FCoE traffic. This PAUSE mechanism is typically implemented for FCoE while regular TCP/IP traffic continues to drop frames. The figure on the slide illustrates how a physical Ethernet link is divided into eight virtual links and allows a PAUSE for a single virtual link without affecting the traffic for the others.

## Slide 66: Enhanced Transmission Selection (ETS)
Allocates bandwidth to different traffic classes such as LAN, SAN, and Inter Process Communication (IPC)
Provides available bandwidth to other classes of traffic when a particular class of traffic does not use its allocated bandwidth
Notes: Enhanced transmission selection (ETS) provides a common management framework for the allocation of bandwidth to different traffic classes, such as LAN, SAN, and Inter Process Communication (IPC). For example, an administrator may assign 40 percent of network bandwidth to LAN traffic, 40 percent of bandwidth to SAN traffic, and 20 percent of bandwidth to IPC traffic. When a particular class of traffic does not use its allocated bandwidth, ETS enables other traffic classes to use the available bandwidth.

## Slide 67: Congestion Notification (CN)
Provides a mechanism for detecting network congestion and notifying the source
  Enables a switch to send a signal to other ports that need to stop or slow down their transmissions
Rate limiting to avoid
packet loss
Congestion
Notification Message
FCoE
Switch
Storage System
(Node B)
Compute
System
(Node A)
Congestion
FCoE
Switch
FCoE
Switch
Notes: Congestion notification (CN) provides end-to-end congestion management for protocols, such as FCoE, that do not have built-in congestion control mechanisms. Link level congestion notification provides a mechanism for detecting congestion and notifying the source to move the traffic flow away from the congested links. Link level congestion notification enables a switch to send a signal to other ports that need to stop or slow down their transmissions. The process of congestion notification and its management is shown on the slide, which represents the communication between the nodes A (sender) and B (receiver). If congestion at the receiving end occurs, the algorithm running on the switch generates a congestion notification message to the sending node (Node A). In response to the message, the sending end limits the rate of data transfer.

## Slide 68: Data Center Bridging Exchange Protocol (DCBX)
Enables CEE devices to convey and configure their features with other CEE devices in the network
  Allows a switch to distribute configuration values to attached network adapters
Ensures consistent configuration across a network
Notes: DCBX is a discovery and capability exchange protocol, which helps CEE devices to convey and configure their features with the other CEE devices in the network. DCBX is used to negotiate capabilities between the switches and the network adapters, which allows the switch to distribute the configuration values to all the attached adapters. This helps to ensure consistent configuration across the entire network.

## Slide 69: Lesson 2: Summary
During this lesson the following topics were covered:
Priority-based flow control
Enhanced transmission selection
Congestion notification
Data center bridging exchange protocol
Notes: This lesson covered Converged Enhanced Ethernet (CEE) and its functionalities – priority-based flow control, enhanced transmission selection, congestion notification, and data center bridging exchange protocol.

## Slide 70: Lesson 3: FCoE Architecture
This lesson covers the following topics:
FCoE frame structure
FCoE frame mapping
FCoE process
FCoE addressing
FCoE frame forwarding
Notes: This lesson covers FCoE frame structure, FCoE frame mapping, FCoE process, FCoE addressing, and FCoE frame forwarding.

## Slide 71: FCoE Frame Structure
FC Frame
Ethernet Frame
FCoE PDU
SOF
EOF
Ethernet Header
FCoE Header
Encapsulated FC Frame (including FC CRC)
FCS
Destination
MAC
Address
Source
MAC
Address
Version
Reserved
VLAN
Tag
Ethertype
Notes: An FCoE frame is an Ethernet frame that contains an FCoE Protocol Data Unit (PDU). The figure on the slide shows the FCoE frame structure. The Ethernet header includes the source and destination MAC addresses, IEEE 802.1Q VLAN tag, and Ethertype field. FCoE has its own Ethertype. The FCoE header includes a version field that identifies the version of FCoE being implemented and some reserved bits. The Start of Frame (SOF) and the End of Frame (EOF) mark the start and the end of the encapsulated FC frame respectively. The encapsulated FC frame consists of the FC header and the data being transported (including the FC CRC). The FCoE frame ends with the Frame Check Sequence (FCS) field that provides error detection for the Ethernet frame. Notice that the FCoE frame, unlike iSCSI and FCIP, has no TCP/IP overhead.
Frame size is an important factor in FCoE. A typical FC data frame has a 2112-byte payload, a 24-byte header, and an FCS. A standard Ethernet frame has a default payload capacity of 1500 bytes. To maintain good performance, FCoE must use jumbo frames to prevent an FC frame from being split into two Ethernet frames.
Note: Jumbo frames
Jumbo frames are Ethernet frames with more than 1500 bytes of payload.

## Slide 72: FCoE Frame Mapping
2 - Data Link
7 - Application
6 - Presentation
5 - Session
4 - Transport
3 - Network
1 - Physical
FC - 4
FC - 3
FC - 2
FCoE Mapping
2 - MAC
1 - Physical
FC - 0 Physical
FC - 1 Data enc/dec
FC - 2 Framing
FC - 3 Services
FC - 4 Protocol map
IEEE 802.3
Layers
FCoE Protocol Stack
OSI Stack
FC Protocol Stack
Ethernet
FC Layers
Notes: The encapsulation of the FC frames occurs through the mapping of the FC frames onto Ethernet, as shown on the slide. FC and traditional networks have stacks of layers where each layer in the stack represents a set of functionalities. The FC stack consists of five layers: FC-0 through FC-4. Ethernet is typically considered as a set of protocols that operates at the physical and data link layers in the seven-layer OSI stack. The FCoE protocol specification replaces the FC-0 and FC-1 layers of the FC stack with Ethernet. This provides the capability to carry the FC-2 to the FC-4 layer over the Ethernet layer.

## Slide 73: FCoE Process
FCoE process includes three key phases:
  Discovery phase:
    FCFs discover each other and form an FCoE fabric
    FCoE nodes find available FCFs for login
    FCoE nodes and FCFs discover potential VN_Port to VF_Port pairing
  Login phase:
    Virtual FC links are created – VN_Port to VF_Port, VE_Port to VE_Port
    VN_Port performs FC login and obtains FC address
    VN_Port obtains a unique MAC address
  Data transfer phase:
    VN_Ports transfer regular FC frames (encapsulated) over CEE network
Notes: To understand the FCoE communication, it is important to know the FCoE process. The FCoE process includes three key phases: discovery, login, and data transfer. These phases are described below:
Discovery phase: In this phase, the FCFs discover each other and form an FCoE fabric. The FCoE nodes also find the available FCFs for login. Moreover, both the FCoE nodes and the FCFs discover potential VN_Port to VF_Port pairing.
Login phase: In this phase, the virtual FC links are established between VN_Ports and VF_Ports as well as between VE_Ports. VN_ports perform FC login (including FLOGI, PLOGI, PRLI) to the discovered FCFs and obtain FC addresses. Each VN_Port also obtains a unique MAC address.
Data transfer phase: After login, the VN_Ports can start transferring regular FC frames (encapsulated) over the CEE network.

## Slide 74: FCoE Initialization Protocol (FIP)
FIP is used for discovering FCFs and establishing virtual links between FCoE nodes and FCoE switches
FIP frames do not transport FC data, but contains discovery and login parameters
Discovery and login use these FIP operations:
  FCoE node sends multicast FIP Solicitation frame to find FCFs for login
  Each FCF replies to FCoE node by sending unicast FIP Advertisement frame
  FCoE node sends FIP FLOGI request to an appropriate FCF
  FCF sends FIP FLOGI Accept containing FC and MAC addresses for VN_Port
Notes: In an FCoE SAN, an FCoE node needs a discovery mechanism that allows it to discover the available FCFs before it can perform FC login. The mechanism used for the discovery is the FCoE Initialization Protocol (FIP). FIP is used for discovering the FCFs and establishing virtual links between FCoE devices (FCoE nodes and FCoE switches). Unlike FCoE frames, FIP frames do not transport FC data, but contain discovery and login/logout parameters. FIP frames are assigned a unique EtherType code to distinguish them from the FCoE frames.
The FCoE node to FCF discovery and the login use the following FIP operations:
FCoE node sends multicast FIP Solicitation frame to find which FCFs are available for login.
Each FCF replies to the FCoE node by sending unicast FIP Advertisement frame.
After the FCoE node decides which FCF is appropriate, it sends FIP FLOGI request to the FCF.
The selected FCF sends FIP FLOGI Accept which contains both FC address and MAC address for the VN_Port. The reason for using FIP for FLOGI instead of a regular FLOGI is that the FIP FLOGI Accept has a field for the FCF to assign a MAC address to the VN_Port.

## Slide 75: FCoE Addressing
An FCoE SAN uses MAC address for frame forwarding
  MAC addresses are assigned to VN_Ports, VF_Ports, and VE_Ports
VF_Ports and VE_Ports obtain MAC addresses from FCoE switch
FCoE supports two types of addressing for VN_Ports:
  Server-provided MAC address (SPMA) and fabric-provided MAC address (FPMA)
Compute systems provide MAC addresses to associated VN_Ports as per Ethernet standards
MAC addresses are either burned-in or are configured by administrators
SPMA
FCoE switches provide MAC addresses to VN_Ports dynamically during node login
MAC address has two parts: 24-bit FC-MAP and 24-bit FC address
FPMA
Notes: An FCoE SAN uses MAC address for frame forwarding. The MAC addresses are assigned to the VN_Ports, VF_Ports, and VE_Ports. The destination and the source MAC addresses are used to direct frames to their Ethernet destinations. Both the VF_Ports and the VE_Ports obtain MAC addresses from the FCoE switch. FCoE supports two types of addressing for the VN_Ports: server-provided MAC address (SPMA) and fabric-provided MAC address (FPMA). These addressing types are described below:
SPMA: In this type of addressing, the compute systems provide MAC addresses to the associated VN_Ports. The MAC addresses are issued in accordance with Ethernet standards. These addresses are either burned-in by the manufacturers of the network adapters or are configured by an administrator. SPMA can use a single MAC address exclusively for FCoE traffic or it can have different MAC address for each VN_Port.
FPMA: In this type of addressing, the VN_Ports receive MAC addresses from the FCoE switches dynamically during login. The VN_Ports then use their granted MAC addresses for communication. This address is derived by concatenating the 24-bit FC MAC address prefix (FC-MAP) and the 24-bit FC address assigned to the VN_Port by the FCoE switch. FC-MAP identifies the fabric to which an FCoE switch belongs. The FPMA ensures that the MAC addresses are unique within an FCoE SAN.

## Slide 76: FCoE Frame Forwarding
To forward frame, a node must know both the MAC address of FCoE switch port and the FC address of destination node port
Compute System
FCoE Switch
FC Switch
CEE Link
Destination = MAC B
Source = MAC A
D_ID = 011C00
S_ID = 050100
D_ID = 011C00
S_ID = 050100
Storage System
FC Link
MAC B
Domain ID = 05
Domain ID = 01
Ethernet Frame with FC Payload
FC Frame
FC Address = 011C00
MAC A
FC Address = 050100
Notes: In an FCoE SAN, a node must know two different addresses to forward a frame to another node. First, it must know the Ethernet MAC address of the FCoE switch port (VF_Port). Second, it must know the FC address assigned to the destination node port (VN_Port or N_Port). The MAC address is used to forward an Ethernet frame containing FC payload over a CEE network. The FC address is used to send the FC frame, encapsulated into the Ethernet frame, to its FC destination.
The figure on the slide shows an example of frame forwarding in the FCoE with existing FC SAN environment. In this example, an FCoE compute system sends an FC frame to an FC storage system. The header part of the FC frame includes the standard FC destination ID (D_ID) and FC source ID (S_ID). The FC frame is encapsulated into an Ethernet frame with a header that includes the destination and source Ethernet MAC addresses. The Ethernet frame is sent to the MAC destination address (MAC B) of the attached FCoE switch having FC domain ID 05. Upon receiving the frame, the FCoE switch strips off the Ethernet frame to retrieve the FC frame. The FC frame is sent without modification to the FC switch with Domain ID = 1, because 01 is the first byte in the D_ID of the FC frame. The FC switch forwards the FC frame to the storage system.

## Slide 77: Lesson 3: Summary
During this lesson the following topics were covered:
FCoE frame structure
FCoE frame mapping
FCoE process
FCoE addressing
FCoE frame forwarding
Notes: This lesson covered FCoE frame structure, FCoE frame mapping, FCoE process, FCoE addressing, and FCoE frame forwarding.

## Slide 78: Module 5: Summary
Key points covered in this module:
FCoE SAN components and connectivity
Converged Enhanced Ethernet functionalities
FCoE architecture
Notes: This module covered FCoE SAN components and connectivity and Converged Enhanced Ethernet (CEE) functionalities – priority-based flow control, enhanced transmission selection, congestion notification, and data center bridging exchange protocol. It also covered FCoE architecture that includes FCoE frame structure, FCoE frame mapping, FCoE process, FCoE addressing, and FCoE frame forwarding.

## Slide 79
Upon completion of this module, you should be able to:
List the third platform requirements for SAN
Describe software-defined networking
Describe FC SAN and its components
Describe FC architecture
Describe FC SAN topologies, link aggregation, and zoning
Describe virtualization in FC SAN environment
Notes: This module focuses on the third platform requirements for SAN, software-defined networking, FC SAN components, FC architecture, FC SAN topologies, link aggregation, and zoning. This module also focuses on virtualization in FC SAN environment.

## Slide 80: Lesson 1: Introduction to SAN
This lesson covers the following topics:
Definition and benefits of SAN
Third platform requirements for SAN
Technology solutions for SAN
Software-defined networking
Notes: This lesson covers the definition and benefits of SAN, third platform requirements for SAN, technology solutions for SAN, and software-defined networking.

## Slide 81: What is a SAN?
A network whose primary purpose is the transfer of data between computer systems and storage devices and among storage devices. - Storage Networking Industry Association
SAN
Client
Client
Clients
Storage Systems
Compute
System
LAN
SAN
Compute
System
Storage Systems
Compute
System
LAN
SAN
Compute
System
WAN
Data Center 1
Data Center 2
NAS
NAS
Notes: Storage area network (SAN) is a network that primarily connects the storage systems with the compute systems and also connects the storage systems with each other. It enables multiple compute systems to access and share storage resources. It also enables data transfer between the storage systems. With long-distance SAN, the data transfer over SAN can be extended across geographic locations. A SAN usually provides access to block-based storage systems.

## Slide 82: Benefits of SAN
Enables both consolidation and sharing of storage resources across multiple compute systems
  Improves utilization of storage resources
  Centralizes management
Enables connectivity across geographically dispersed locations
  Enables compute systems across locations to access shared data
  Enables replication of data between storage systems that reside in separate locations
  Facilitates remote backup of application data
Notes: SANs address the limitations of direct-attached storage (DAS) environment. Unlike a DAS environment, where the compute systems own the storage, SANs enable both consolidation and sharing of storage resources across multiple compute systems. This improves the utilization of storage resources compared to a DAS environment and reduces the total amount of storage that an organization needs to purchase and manage. With consolidation, storage management becomes centralized and less complex, which further reduces the cost of managing information.
A SAN may span over wide locations. This enables organizations to connect geographically dispersed compute systems and storage systems. The long-distance SAN connectivity enables the compute systems across locations to access shared data. The long-distance connectivity also enables the replication of data between storage systems that reside in separate locations. The replication over long-distances helps in protecting data against local and regional disaster. Further, the long-distance SAN connectivity facilitates remote backup of application data. Backup data can be transferred through a SAN to a backup device that may reside at a remote location. This avoids having to ship tapes (backup media) from the primary site to the remote site and the associated pitfalls such as packing and shipping expenses and lost tapes in transit.

## Slide 83: Third Platform Requirements for SAN
An effective SAN infrastructure must provide:
  High throughput to support high performance computing
  Interconnectivity among a large number of devices over wide locations to transfer massively distributed, high volume of data
  Elastic and non-disruptive scaling to support applications that are horizontally scaled
  Automated and policy-driven infrastructure configuration
  Simplified, flexible, and agile management operations
Notes: The IT industry is in the middle of a massive technological and structural shift toward what the industry analyst IDC calls the third platform. Third platform is built on social networking, mobile computing, cloud services, and big data analytics technologies. Applications that support these technologies require significantly higher performance, scalability, and availability compared to the traditional applications. Similar to the compute and storage infrastructure, the SAN infrastructure must also be ready to support the requirements of third platform applications. Therefore, it is necessary to establish how the third platform application requirements are translated into the SAN requirements. This slide provides a list of key requirements for an effective SAN infrastructure.

## Slide 84: Technology Solutions
Software-defined networking
SAN implementations:
  Fibre Channel (FC) SAN
  Internet Protocol (IP) SAN
  Fibre Channel over Ethernet (FCoE) SAN
Virtualization in SAN
Notes: Technology solutions that can meet the third platform requirements for the SANs are:
Software-defined networking
SAN implementations:
  Fibre Channel (FC) SAN
  Internet Protocol (IP) SAN
  Fibre Channel over Ethernet (FCoE) SAN
Virtualization in SAN
Both the software-defined networking and the FC SAN are covered in this module. Module 10, ‘Internet Protocol (IP) SAN’ and module 11, ‘FC over Ethernet (FCoE) SAN’ describe IP SAN and FCoE SAN respectively. Virtualization in SAN is described along with each of the SAN implementations.

## Slide 85: Software-Defined Networking
Abstracts and separates control plane from data plane
Software (controller) external to the network components takes over control functions
Controller sends instructions for data plane at the network component to handle network traffic
Network Components (Data Plane)
Switch
Network Controller (Control Plane)
Programming Logic for Switching Network Traffic
Switch
Switch
Switch
Switch
Interaction
Notes: Traditionally, a network component such as a switch or a router consists of a data plane and a control plane. These planes are implemented in the firmware of the network components. The function of the data plane is to transfer the network traffic from one physical port to another port by following rules that are programmed into the component. The function of the control plane is to provide the programming logic that the data plane follows for switching or routing of the network traffic. Software-defined networking is an approach to abstract and separate the control plane functions from the data plane functions. Instead of the built-in control functions at the network components level, the software external to the components takes over the control functions. The software runs on a compute system or a standalone device and is called network controller. The network controller interacts with the network components to gather configuration information and to provide instructions for data plane in order to handle the network traffic.

## Slide 86: Benefits of Software-Defined SAN
Centralized control
  Single point of control for SAN infrastructure
Policy-based automation
  Management operations are programmed in the network controller based on business policies
Simplified, agile management
  Management functions are simplified through abstraction of operational complexity
Notes: Software-defined networking in the SAN provides several benefits. These are described below:
Centralized control: The software-defined approach provides a single point of control for the entire SAN infrastructure that may span across data centers. The centralized control plane provides that programming logic for transferring the SAN traffic, which can be uniformly and quickly applied across the SAN infrastructure. The programming logic can be upgraded centrally to add new features and based on application requirements.
Policy-based automation: With software-defined approach, many hardware-based SAN management operations such as zoning (described later) can be automated. Management operations may be programmed in the network controller based on business policies and best practices. This reduces the need for manual operations that are repetitive, error-prone, and time-consuming. Policy-based automation also helps to standardize the management operations.
Simplified, agile management: The network controller usually provides a management interface that includes a limited and standardized set of management functions. With policy-based automation in place, these management functions are available in simplified form, abstracting the underlying operational complexity. This makes it easy to configure a SAN infrastructure. This also helps promptly modifying the SAN configuration to respond to the changing application requirements.

## Slide 87: Lesson 1: Summary
During this lesson the following topics were covered:
Definition and benefits of SAN
Third platform requirements for SAN
Technology solutions for SAN
Software-defined networking
Notes: This lesson covered the definition and benefits of SAN, third platform requirements for SAN, technology solutions for SAN, and software-defined networking.

## Slide 88: Lesson 2: FC SAN Overview
This lesson covers the following topics:
Components of FC SAN
FC interconnectivity options
FC port types
Notes: This lesson covers the components of FC SAN, three FC interconnectivity options, and FC port types.

## Slide 89: What is FC SAN?
A SAN that uses Fibre Channel (FC) protocol for communication
Supports data transmission speed up to 16 Gb/s
Enables data transmission without dropping frames
Provides high scalability
  Theoretically, accommodate approximately 15 million devices
Storage Systems
Compute Systems
FC SAN
Notes: Fibre Channel SAN (FC SAN) uses Fibre Channel (FC) protocol for communication. FC protocol (FCP) is used to transport data, commands, and status information between the compute systems and the storage systems. It is also used to transfer data between the storage systems.
FC is a high-speed network technology that runs on high-speed optical fiber cables and serial copper cables. The FC technology was developed to meet the demand for the increased speed of data transfer between compute systems and mass storage systems. In comparison with Ultra-Small Computer System Interface (Ultra-SCSI) that is commonly used in the DAS environments, FC is a significant leap in storage networking technology. The latest FC implementations of 16 GFC offer a throughput of 3200 MB/s (raw bit rates of 16 Gb/s), whereas Ultra640 SCSI is available with a throughput of 640 MB/s. FC is expected to come with 6400 MB/s (raw bit rates of 32 Gb/s) and 25600 MB/s (raw bit rates of 128 Gb/s) throughput in 2016. Technical Committee T11, which is the committee within International Committee for Information Technology Standards (INCITS), is responsible for FC interface standards.
FC supports credit-based flow control mechanism (described later). The flow control mechanism delivers data as fast as the destination buffer is able to receive it, without dropping frames. FC also has very little transmission overhead. The FC architecture is highly scalable, and theoretically, a single FC SAN can accommodate approximately 15 million devices.
Note: FibRE refers to the protocol, whereas fibER refers to a media.

## Slide 90: Components of FC SAN
Network adapters
  FC HBAs in compute system
  Front-end adapters in storage system
Cables
  Copper cables for short distance
  Optical fiber cables for long distance
    Two types: multimode and single-mode
Interconnecting devices
  FC hubs, FC switches, and FC directors
Multimode Fiber
Single-mode Fiber
Notes: The key FC SAN components are network adapters, cables, and interconnecting devices. These components are described below.
Network adapters: In an FC SAN, the end devices, such as compute systems and storage systems are all referred to as nodes. Each node is a source or destination of information. Each node requires one or more network adapters to provide a physical interface for communicating with other nodes. Examples of network adapters are FC host bus adapters (HBAs) and storage system front-end adapters. An FC HBA has SCSI-to-FC processing capability. It encapsulates OS or hypervisor storage I/Os (usually SCSI I/O) into FC frames before sending the frames to the FC storage systems over an FC SAN.
Cables: FC SAN implementations primarily use optical fiber cabling. Copper cables may be used for shorter distances because it provides acceptable signal-to-noise ratio for distances up to 30 meters. Optical fiber cables carry data in the form of light. There are two types of optical cables: multimode and single-mode. Multimode fiber (MMF) cable carries multiple beams of light projected at different angles simultaneously onto the core of the cable. In an MMF transmission, multiple light beams traveling inside the cable tend to disperse and collide. This collision weakens the signal strength after it travels a certain distance – a process known as modal dispersion. Due to modal dispersion, an MMF cable is typically used for short distances, commonly within a data center. Single-mode fiber (SMF) carries a single ray of light projected at the center of the core. The small core and the single light wave help to limit modal dispersion. Single-mode provides minimum signal attenuation over maximum distance (up to 10 km). A single-mode cable is used for long-distance cable runs, and the distance usually depends on the power of the laser at the transmitter and the sensitivity of the receiver. A connector is attached at the end of a cable to enable swift connection and disconnection of the cable to and from a port. A standard connector (SC) and a lucent connector (LC) are two commonly used connectors for fiber optic cables.
Interconnecting devices: The commonly used interconnecting devices in FC SANs are FC hubs, FC switches, and FC directors. These devices are further detailed in the next slide.

## Slide 91: Hub, Switch, and Director
FC Hub | FC Switch | FC Director
Nodes are connected in a logical loop Nodes share loop Provides limited connectivity and scalability | Each node has a dedicated communication path Provides a fixed port count ─ active or unused Active ports can be scaled-up non-disruptively Some components are redundant and hot-swappable | High-end switches with a higher port count Has a modular architecture Port count is scaled-up by inserting line cards/blades All key components are redundant and hot-swappable
Notes: FC hubs are used as communication devices in Fibre Channel Arbitrated Loop (FC-AL) implementations (discussed later). Hubs physically connect nodes in a logical loop or a physical star topology. All the nodes must share the loop because data travels through all the connection points. Because of the availability of low-cost and high-performance switches, the FC switches are preferred over the FC hubs in FC SAN deployments.
FC switches are more intelligent than FC hubs and directly route data from one physical port to another. Therefore, the nodes do not share the data path. Instead, each node has a dedicated communication path. The FC switches are commonly available with a fixed port count. Some of the ports can be active for operational purpose and the rest remain unused. The number of active ports can be scaled-up non-disruptively. Some of the components of a switch such as power supplies and fans are redundant and hot-swappable (components can be replaced while a device is powered-on and remains in operation).
FC directors are high-end switches with a higher port count. A director has a modular architecture and its port count is scaled-up by inserting additional line cards or blades to the director’s chassis. Directors contain redundant components with automated failover capability. Its key components such as switch controllers, blades, power supplies, and fan modules are all hot-swappable. These insure high availability for business critical applications.

## Slide 92: FC Interconnectivity Options
Point-to-point: Enables direct connection between two nodes
FC arbitrated loop (FC-AL): Provides shared loop to the attached nodes
FC switched fabric (FC-SW): Nodes communicate with one another using switches
Storage
System
Compute
System
Storage
System
Compute
Systems
FC Switch
FC Switch
Interswitch Links
Compute
System
FC Hub
Compute
System
Storage
System
Compute
System
Notes: The FC architecture supports three basic interconnectivity options: point-to-point, fibre channel arbitrated loop (FC-AL), and fibre channel switched fabric (FC-SW). These interconnectivity options are described below:
Point-to-point: In this configuration, two nodes are connected directly to each other. This configuration provides a dedicated connection for data transmission between nodes. However, the point-to-point configuration offers limited connectivity and scalability and is used in a DAS environment.
FC-AL: In this configuration, the devices are attached to a shared loop. Each device contends with other devices to perform I/O operations. The devices on the loop must “arbitrate” to gain control of the loop. At any given time, only one device can perform I/O operations on the loop. Because each device in a loop must wait for its turn to process an I/O request, the overall performance in FC-AL environments is low. Further, adding or removing a device results in loop re-initialization, which can cause a momentary pause in loop traffic. As a loop configuration, FC-AL can be implemented without any interconnecting devices by directly connecting one device to another two devices in a ring through cables. However, FC-AL implementations may also use FC hubs through which the arbitrated loop is physically connected in a star topology.
FC-SW: It involves a single FC switch or a network of FC switches (including FC directors) to interconnect the nodes. It is also referred to as fabric connect. A fabric is a logical space in which all nodes communicate with one another in a network. In a fabric, the link between any two switches is called an interswitch link (ISL). ISLs enable switches to be connected together to form a single, larger fabric. They enable the transfer of both storage traffic and fabric management traffic from one switch to another. In FC-SW, nodes do not share a loop; instead, data is transferred through a dedicated path between the nodes. Unlike a loop configuration, an FC-SW configuration provides high scalability. The addition or removal of a node in a switched fabric is minimally disruptive; it does not affect the ongoing traffic between other nodes.

## Slide 93: Port Types in Switched Fabric
Compute System
N_Port
FC Switch
F_Port
FC Switch
Storage System
N_Port
F_Port
E_Port
E_Port
Storage System
N_Port
F_Port
ISL
Notes: The ports in a switched fabric can be one of the following types:
  N_Port: It is an end point in the fabric. This port is also known as the node port. Typically, it is a compute system port (FC HBA port) or a storage system port that is connected to a switch in a switched fabric.
  E_Port: It is a port that forms the connection between two FC switches. This port is also known as the expansion port. The E_Port on an FC switch connects to the E_Port of another FC switch in the fabric ISLs.
  F_Port: It is a port on a switch that connects an N_Port. It is also known as a fabric port.
  G_Port: It is a generic port on a switch that can operate as an E_Port or an F_Port and determines its functionality automatically during initialization.

## Slide 94: Lesson 2: Summary
During this lesson the following topics were covered:
Components of FC SAN
FC interconnectivity options
FC port types
Notes: This lesson covered FC SAN components, three FC interconnectivity options, and various FC port types.

## Slide 95: Lesson 3: Fibre Channel (FC) Architecture
This lesson covers the following topics:
FC protocol stack
FC and WWN addressing
Structure and organization of FC data
Fabric services
Fabric login types
Flow control
Notes: This lesson covers FC protocol stack, FC and WWN addressing, and structure and organization of FC data. This lesson also covers fabric services, fabric login types, and flow control.

## Slide 96: FC Architecture Overview
Provides benefits of both channel and network technologies
  Provides high performance with low protocol overheads
  Provides high scalability with long distance capability
Implements SCSI over FC network
  Transports SCSI data through FC network
Storage devices, attached to FC SAN, appear as locally attached to the OS or hypervisor
Notes: Traditionally, compute operating systems have communicated with peripheral devices over channel connections, such as Enterprise Systems Connection (ESCON) and SCSI. Channel technologies provide high levels of performance with low protocol overheads. Such performance is achievable due to the static nature of channels and the high level of hardware and software integration provided by the channel technologies. However, these technologies suffer from inherent limitations in terms of the number of devices that can be connected and the distance between these devices.
In contrast to channel technology, network technologies are more flexible and provide greater distance capabilities. Network connectivity provides greater scalability and uses shared bandwidth for communication. This flexibility results in greater protocol overhead and reduced performance.
The FC architecture represents true channel and network integration and captures some of the benefits of both channel and network technology. FC protocol provides both the channel speed for data transfer with low protocol overhead and the scalability of network technology. FC provides a serial data transfer interface that operates over copper wire and optical fiber.
  FC protocol forms the fundamental construct of the FC SAN infrastructure. FC protocol predominantly is the implementation of SCSI over an FC network. SCSI data is encapsulated and transported within FC frames. SCSI over FC overcomes the distance and the scalability limitations associated with traditional direct-attached storage. Storage devices attached to the FC SAN appear as locally attached devices to the operating system (OS) or hypervisor running on the compute system.

## Slide 97: FC Protocol Stack
1 Gb/s
2 Gb/s
4 Gb/s
16 Gb/s
FC-4
FC-2
FC-1
FC-0
Upper Layer Protocol
Example: SCSI, HIPPI, ESCON, ATM, IP
Framing/Flow Control
Encode/Decode
8 Gb/s
Upper Layer Protocol Mapping
FC Layer | Function | Features Specified by FC Layer
FC-4 | Mapping interface | Mapping upper layer protocol (e.g. SCSI) to lower FC layers
FC-3 | Common services | Not implemented
FC-2 | Routing, flow control | Frame structure, FC addressing, flow control
FC-1 | Encode/decode | 8b/10b or 64b/66b encoding, bit and frame synchronization
FC-0 | Physical layer | Media, cables, connector
Notes: It is easier to understand a communication protocol by viewing it as a structure of independent layers. FCP defines the communication protocol in five layers: FC-0 through FC-4 (except FC-3 layer, which is not implemented).
FC-4 Layer: It is the uppermost layer in the FCP stack. This layer defines the application interfaces and the way Upper Layer Protocols (ULPs) are mapped to the lower FC layers. The FC standard defines several protocols that can operate on the FC-4 layer. Some of the protocols include SCSI, High Performance Parallel Interface (HIPPI) Framing Protocol, ESCON, Asynchronous Transfer Mode (ATM), and IP.
FC-2 Layer: It provides FC addressing, structure, and organization of data (frames, sequences, and exchanges). It also defines fabric services, classes of service, flow control, and routing.
FC-1 Layer: It defines how data is encoded prior to transmission and decoded upon receipt. At the transmitter node, an 8-bit character is encoded into a 10-bit transmission character. This character is then transmitted to the receiver node. At the receiver node, the 10-bit character is passed to the FC-1 layer, which decodes the 10-bit character into the original 8-bit character. FC links, with a speed of 10 Gbps and above, use 64-bit to 66-bit encoding algorithm. This layer also defines the transmission words such as FC frame delimiters, which identify the start and the end of a frame and the primitive signals that indicate events at a transmitting port. In addition to these, the FC-1 layer performs link initialization and error recovery.
FC-0 Layer: It is the lowest layer in the FCP stack. This layer defines the physical interface, media, and transmission of bits. The FC-0 specification includes cables, connectors, and optical and electrical parameters for a variety of data rates. The FC transmission can use both electrical and optical media.

## Slide 98: FC Addressing in Switched Fabric
FC address is assigned to node ports during fabric login
  Used for communication between nodes in an FC SAN
Address format:
Domain ID is a unique number provided to each switch in the fabric
  239 addresses are available for domain ID
Maximum possible number of node ports in a switched fabric:
  239 domains X 256 areas X 256 ports = 15,663,104 ports
Notes: An FC address is dynamically assigned when a node port logs on to the fabric. The FC address has a distinct format, as shown on the slide. The first field of the FC address contains the domain ID of the switch. A domain ID is a unique number provided to each switch in the fabric. Although this is an 8-bit field, there are only 239 available addresses for domain ID because some addresses are deemed special and reserved for fabric services. For example, FFFFFC is reserved for the name server, and FFFFFE is reserved for the fabric login service. The area ID is used to identify a group of switch ports used for connecting nodes. An example of a group of ports with common area ID is a port card on the switch. The last field, the port ID, identifies the port within the group.
Therefore, the maximum possible number of node ports in a switched fabric is calculated as:
239 domains X 256 areas X 256 ports = 15,663,104 ports.

## Slide 99: World Wide Name (WWN)
Unique 64-bit identifier
Static to node ports on an FC network
  Similar to MAC address of NIC
  WWNN and WWPN are used to physically identify FC network adapters and node ports respectively
Notes: Each device in the FC environment is assigned a 64-bit unique identifier called the World Wide Name (WWN). The FC environment uses two types of WWNs: World Wide Node Name (WWNN) and World Wide Port Name (WWPN). WWNN is used to physically identify FC network adapters and WWPN is used to physically identify FC adapter ports or node ports. For example, a dual-port FC HBA has one WWNN and two WWPNs.
Unlike an FC address, which is assigned dynamically, a WWN is a static name for each device on an FC network. WWNs are similar to the Media Access Control (MAC) addresses used in IP networking. WWNs are burned into the hardware or assigned through software. Several configuration definitions in an FC SAN use WWN for identifying storage systems and FC HBAs. WWNs are critical for FC SAN configuration as each node port has to be registered by its WWN before the FC SAN recognizes it. The name server in an FC SAN environment keeps the association of WWNs to the dynamically created FC addresses for node ports. The figure on the slide illustrates the WWN structure examples for a storage system and an HBA.

## Slide 100: Structure and Organization of FC Data
FC data is organized as Exchange, Sequence, and Frame
FC Data Structure | Description
Exchange | Enables two N_Ports to identify and manage a set of information units Information unit: upper layer protocol-specific information that is sent to another port to perform certain operation Each information unit maps to a sequence Includes one or more sequences
Sequence | Contiguous set of frames that correspond to an information unit
Frame | Fundamental unit of data transfer Each frame consists of five parts: SOF, frame header, data field, CRC, and EOF
SOF
4 Bytes
Data Field
0 - 2112 Bytes
CRC
4 Bytes
EOF
4 Bytes
Frame Header
24 Bytes
Notes: In an FC network, data transport is analogous to a conversation between two people, whereby a frame represents a word, a sequence represents a sentence, and an exchange represents a conversation.
Exchange: An exchange operation enables two node ports to identify and manage a set of information units. Each upper layer protocol (ULP) has its protocol-specific information that must be sent to another port to perform certain operations. This protocol-specific information is called an information unit. The structure of these information units is defined in the FC-4 layer. This unit maps to a sequence. An exchange is composed of one or more sequences.
Sequence: A sequence refers to a contiguous set of frames that are sent from one port to another. A sequence corresponds to an information unit, as defined by the ULP.
Frame: A frame is the fundamental unit of data transfer at FC-2 layer. An FC frame consists of five parts: start of frame (SOF), frame header, data field, cyclic redundancy check (CRC), and end of frame (EOF). The SOF and EOF act as delimiters. The frame header is 24 bytes long and contains addressing information for the frame. The data field in an FC frame contains the data payload, up to 2,112 bytes of actual data – in most cases the SCSI data. The CRC checksum facilitates error detection for the content of the frame. This checksum verifies data integrity by checking whether the content of the frames are received correctly. The CRC checksum is calculated by the sender before encoding at the FC-1 layer. Similarly, it is calculated by the receiver after decoding at the FC-1 layer.

## Slide 101: Fabric Services
FC switches provide fabric services as defined in FC standards
Fabric Services | Description
Fabric Login Server | Used during the initial part of the node’s fabric login process Located at pre-defined address of FFFFFE
Name Server | Responsible for name registration and management of node ports Located at pre-defined address FFFFFC
Fabric Controller | Responsible for managing and distributing Registered State Change Notifications (RSCNs) to attached node ports Responsible for distributing SW-RSCNs to every other switch Located at pre-defined address FFFFFD
Management Server | Enables FC SAN management using fabric management software Located at pre-defined address FFFFFA
Notes: All FC switches, regardless of the manufacturer, provide a common set of services as defined in the FC standards. These services are available at certain predefined addresses. Some of these services are Fabric Login Server, Fabric Controller, Name Server, and Management Server.
Fabric Login Server: It is located at the predefined address of FFFFFE and is used during the initial part of the node’s fabric login process.
Name Server (formally known as Distributed Name Server): It is located at the predefined address FFFFFC and is responsible for name registration and management of node ports. Each switch exchanges its Name Server information with other switches in the fabric to maintain a synchronized, distributed name service.
Fabric Controller: Each switch has a Fabric Controller located at the predefined address FFFFFD. The Fabric Controller provides services to both node ports and other switches. The Fabric Controller is responsible for managing and distributing Registered State Change Notifications (RSCNs) to the node ports registered with the Fabric Controller. If there is a change in the fabric, RSCNs are sent out by a switch to the attached node ports. The Fabric Controller also generates Switch Registered State Change Notifications (SW-RSCNs) to every other domain (switch) in the fabric. These RSCNs keep the name server up-to-date on all switches in the fabric.
Management Server: FFFFFA is the FC address for the Management Server. The Management Server is distributed to every switch within the fabric. The Management Server enables the FC SAN management software to retrieve information and administer the fabric.

## Slide 102: Fabric Login Types
Fabric login (FLOGI)
  Occurs between an N_Port and an F_Port
  Node sends a FLOGI frame with WWN to Fabric Login Server on switch
  Node obtains FC address from switch
  Immediately after FLOGI, N_Port registers with Name Server on switch
  N_Port queries name server about all other logged in ports
Port login (PLOGI)
  Occurs between two N_Ports to establish a session
  Exchange service parameters relevant to the session
Process login (PRLI)
  Occurs between two N_Ports to exchange ULP related parameters
Notes: Fabric services define three login types:
  Fabric login (FLOGI): It is performed between an N_Port and an F_Port. To log on to the fabric, a node sends a FLOGI frame with the WWNN and WWPN parameters to the login service at the predefined FC address FFFFFE (Fabric Login Server). In turn, the switch accepts the login and returns an Accept (ACC) frame with the assigned FC address for the node. Immediately after the FLOGI, the N_Port registers itself with the local Name Server on the switch, indicating its WWNN, WWPN, port type, class of service, assigned FC address, and so on. After the N_Port has logged in, it can query the name server database for information about all other logged in ports.
  Port login (PLOGI): It is performed between two N_Ports to establish a session. The initiator N_Port sends a PLOGI request frame to the target N_Port, which accepts it. The target N_Port returns an ACC to the initiator N_Port. Next, the N_Ports exchange service parameters relevant to the session.
  Process login (PRLI): It is also performed between two N_Ports. This login relates to the FC-4 ULPs, such as SCSI. If the ULP is SCSI, N_Ports exchange SCSI-related service parameters.

## Slide 103: Flow Control
Fabric uses BB_Credit for flow control between FC port pairs
  Occurs between an N_Port and an F_Port, and between two E_Ports
  Credit value is negotiated based on receiving port’s capability
  R_RDY is used for acknowledgment
R_RDY
Data Frame
R_RDY
Data Frame
R_RDY
Data Frame
FC Switch
FC Switch
Storage System
Compute System
Notes: Flow control is the process to regulate the data transmission rate between two devices so that a transmitting device does not overflow a receiving device with data. A fabric uses the buffer-to-buffer credit (BB_Credit) mechanism for flow control. The BB_Credit management may occur between any two FC ports.
In a fabric, an FC frame is received and stored in a receive buffer where it is processed by the receiving FC port. If another frame arrives while the receiving port is processing the first frame, a second receive buffer is needed to hold the new frame. If all the receive buffers are filled up with received frames and the transmitting port sends another frame, then the receiving port would not have a receive buffer available to hold the new frame and the frame would be dropped. BB_Credit mechanism ensures that the FC ports do not run out of buffers and do not drop frames.
With BB_Credit mechanism, the transmitting and receiving ports agree on the number of buffers available or BB_Credits during the port login process. The credit value is decremented when a frame is transmitted and incremented upon receiving a response. A receiver ready (R_RDY) is sent from the receiving port to the transmitting port for every free buffer on the receiving side. The transmitting port increments the credit value per R_RDY it receives from the receiving port. The transmitting port maintains a count of available credits and continues to send frames if the count is greater than zero. If the available credits reaches zero, then further transmission of frames is suspended until the credit count becomes a nonzero value.
In the figure shown on the slide, a data frame is sent from the N_Port of a compute system to the F_Port of an FC switch. Once the frame is processed and passes the F_Port, the buffer is released and an R_RDY is sent to the transmitting N_Port, allowing the buffer to be marked as available. Each port-to-port data transmission occurs in this manner throughout the fabric.

## Slide 104: Lesson 3: Summary
During this lesson the following topics were covered:
FC protocol stack
FC and WWN addressing
Structure and organization of FC data
Fabric services
Fabric login types
Flow control
Notes: This lesson covered FC protocol stack, FC and WWN addressing, and structure and organization of FC data. This lesson also covered fabric services, fabric login types, and flow control.

## Slide 105: Lesson 4: Topologies, Link Aggregation, and Zoning
This lesson covers the following topics:
Single-switch topology
Mesh topology
Core-edge topology
Link aggregation
Types of zoning
Notes: This lesson covers FC SAN topologies such as single-switch, mesh, and core-edge. This lesson also covers link aggregation and types of zoning.

## Slide 106: Single-switch Topology
Fabric consists of only a single switch
Both compute systems and storage systems connect to same switch
No ISLs are required for compute-to-storage traffic
Every switch port is usable for node connectivity
FC Director
Storage System
Compute
System
Single Switch Fabric
Compute
System
Notes: FC switches (including FC directors) may be connected in a number of ways to form different fabric topologies. Each topology provides certain benefits.
In a single-switch topology, the fabric consists of only a single switch. Both the compute systems and the storage systems are connected to the same switch. A key advantage of a single-switch fabric is that it does not need to use any switch port for ISLs. Therefore, every switch port is usable for compute system or storage system connectivity. Further, this topology helps eliminate FC frames traveling over the ISLs and consequently eliminates the ISL delays.
A typical implementation of a single-switch fabric would involve the deployment of an FC director. FC directors are high-end switches with a high port count. When additional switch ports are needed over time, new ports can be added via add-on line cards (blades) in spare slots available on the director chassis. To some extent, a bladed solution alleviates the port count scalability problem inherent in a single-switch topology.

## Slide 107: Mesh Topology
Full mesh
  Each switch is connected to every other switch
  Maximum of one ISL is required for compute-to-storage traffic
  Compute systems and storage systems can be connected to any switch
Partial mesh
  Not all the switches are connected to every other switch
Storage Array
FC Switches
Storage
System
Compute
System
Full Mesh Fabric
Compute
System
FC Switches
Storage
System
Compute
System
Partial Mesh Fabric
Compute
System
Notes: A mesh topology may be one of the two types: full mesh or partial mesh. In a full mesh, every switch is connected to every other switch in the topology. A full mesh topology may be appropriate when the number of switches involved is small. A typical deployment would involve up to four switches or directors, with each of them servicing highly localized compute-to-storage traffic. In a full mesh topology, a maximum of one ISL or hop is required for compute-to-storage traffic. However, with the increase in the number of switches, the number of switch ports used for ISL also increases. This reduces the available switch ports for node connectivity.
In a partial mesh topology, not all the switches are connected to every other switch. In this topology, several hops or ISLs may be required for the traffic to reach its destination. Partial mesh offers more scalability than full mesh topology. However, without proper placement of compute and storage systems, traffic management in a partial mesh fabric might be complicated and ISLs could become overloaded due to excessive traffic aggregation.

## Slide 108: Core-edge Topology
Consists of edge and core switch tiers
Storage systems are usually connected to the core tier
Maximum of one ISL is required for compute-to-storage traffic
Fabric can be scaled to a larger environment by adding more core and edge switches
FC Switch
FC Switch
FC Switch
Storage System
FC Director
Compute System
Edge Tier
Core Tier
Notes: The core-edge topology has two types of switch tiers: edge and core.
The edge tier is usually composed of switches and offers an inexpensive approach to adding more compute systems in a fabric. The edge-tier switches are not connected to each other. Each switch at the edge tier is attached to a switch at the core tier through ISLs.
The core tier is usually composed of directors that ensure high fabric availability. In addition, typically all traffic must either traverse this tier or terminate at this tier. In this configuration, all storage systems are connected to the core tier, enabling compute-to-storage traffic to traverse only one ISL. Compute systems that require high performance may be connected directly to the core tier and consequently avoid ISL delays.
The core-edge topology increases connectivity within the FC SAN while conserving the overall port utilization. It eliminates the need to connect edge switches to other edge switches over ISLs. Reduction of ISLs can greatly increase the number of node ports that can be connected to the fabric. If fabric expansion is required, then administrators would need to connect additional edge switches to the core. The core of the fabric is also extended by adding more switches or directors at the core tier. Based on the number of core-tier switches, this topology has different variations, such as single-core topology and dual-core topology. To transform a single-core topology to dual-core, new ISLs are created to connect each edge switch to the new core switch in the fabric.

## Slide 109: Link Aggregation
Combines multiple ISLs into a single logical ISL (port-channel)
  Provides higher throughput than a single ISL could provide
  Distributes network traffic over ISLs, ensuring even ISL utilization
H1-5 Gb/s
H2-1.5 Gb/s
H3-2 Gb/s
H4-4.5 Gb/s
S1-5 Gb/s
S2-1.5 Gb/s
S3-2 Gb/s
S4-4.5 Gb/s
{H1,S1}
{H4,S4}
{H2,S2}
{H3,S3}
3 ISLs (No Aggregation)
ISL Bandwidth = 8 Gb/s
FC Switch
FC Switch
H1-5 Gb/s
H2-1.5 Gb/s
H3-2 Gb/s
H4-4.5 Gb/s
S1-5 Gb/s
S2-1.5 Gb/s
S3-2 Gb/s
S4-4.5 Gb/s
{H1,S1}
{H4,S4}
{H2,S2}
{H3,S3}
ISL Aggregation
Port-Channel Bandwidth = 24 Gb/s
FC Switch
FC Switch
Notes: Link aggregation combines two or more parallel ISLs into a single logical ISL, called a port-channel, yielding higher throughput than a single ISL could provide. For example, the aggregation of 10 ISLs into a single port-channel provides up to 160 Gb/s throughput assuming the bandwidth of an ISL is 16 Gb/s. Link aggregation optimizes fabric performance by distributing network traffic across the shared bandwidth of all the ISLs in a port-channel. This allows the network traffic for a pair of node ports to flow through all the available ISLs in the port-channel rather than restricting the traffic to a specific, potentially congested ISL. The number of ISLs in a port channel can be scaled depending on application’s performance requirement.
This slide illustrates two examples. The example on the left is based on an FC SAN infrastructure with no link aggregation enabled. Four HBA ports H1, H2, H3, and H4 have been configured to generate I/O activity to four storage system ports S1, S2, S3, and S4 respectively. The HBAs and the storage systems are connected to two separate FC switches with three ISLs between the switches. Let us assume that the bandwidth of each ISL is 8 Gb/s and the data transmission rate for the port-pairs {H1,S1}, {H2,S2}, {H3,S3}, and {H4,S4} are 5 Gb/s, 1.5 Gb/s, 2 Gb/s, and 4.5 Gb/s. Without link aggregation, the fabric typically assigns a particular ISL for each of the port-pairs in a round-robin fashion. It is possible that port-pairs {H1,S1} and {H4,S4} are assigned to the same ISL in their respective routes. The other two ISLs are assigned to the port-pairs {H2,S2} and {H3,S3}. Two of the three ISLs are under-utilized, whereas the third ISL is saturated and becomes a performance bottleneck for the port-pairs assigned to it. The example on the right has aggregated the three ISLs into a port-channel that provides throughput up to 24 Gb/s. Network traffic for all the port-pairs are distributed over the ISLs in the port-channel, which ensures even ISL utilization.

## Slide 110: Zoning
Zone set comprises zones
Each zone comprises zone members (FC HBA and storage system ports)
Benefits:
  Restricts RSCN traffic
  Provides access control
Storage
System
Compute System
Storage
System
Port
FC HBA Port
Zone 1
Zone 2
Compute System
FC SAN
An FC switch function that enables node ports within the fabric to be logically segmented into groups, and communicate with each other within the group.
Zoning
Notes: Zoning is an FC switch function that enables node ports within the fabric to be logically segmented into groups and communicate with each other within the group.
Whenever a change takes place in the name server database, the fabric controller sends a Registered State Change Notification (RSCN) to all the nodes impacted by the change. If zoning is not configured, the fabric controller sends the RSCN to all the nodes in the fabric. Involving the nodes that are not impacted by the change increases the amount of fabric-management traffic. For a large fabric, the amount of FC traffic generated due to this process can be significant and might impact the compute-to-storage data traffic. Zoning helps to limit the number of RSCNs in a fabric. In the presence of zoning, a fabric sends the RSCN to only those nodes in a zone where the change has occurred.
Zoning also provides access control, along with other access control mechanisms, such as LUN masking. Zoning provides control by allowing only the members in the same zone to establish communication with each other.
Zone members, zones, and zone sets form the hierarchy defined in the zoning process. A zone set is composed of a group of zones that can be activated or deactivated as a single entity in a fabric. Multiple zone sets may be defined in a fabric, but only one zone set can be active at a time. Members are the nodes within the FC SAN that can be included in a zone. FC switch ports, FC HBA ports, and storage system ports can be members of a zone. A port or node can be a member of multiple zones. Nodes distributed across multiple switches in a switched fabric may also be grouped into the same zone. Zone sets are also referred to as zone configurations.

## Slide 111: Types of Zoning
WWN Zoning, Port Zoning, Mixed Zoning
Zone 2
Zone 3
Port 1
Port 5
WWN 10:00:00:00:C9:20:DC:40
WWN 10:00:00:00:C9:20:DC:56
WWN 10:00:00:00:C9:20:DC:82
WWN 50:06:04:82:E8:91:2B:9E
Zone 1 (WWN Zone) = 10:00:00:00:C9:20:DC:82 ; 50:06:04:82:E8:91:2B:9E
Zone 2 (Port Zone) = 15,5 ; 15,12
Zone 3 (Mixed Zone) = 10:00:00:00:C9:20:DC:56 ; 15,12
Compute
System
Storage System
FC
Switch
Switch Domain ID = 15
Zone 1
Port 12
Port 9
Compute
System
Compute
System
Notes: Zoning can be categorized into three types:
  WWN zoning: It uses World Wide Names to define zones. The zone members are the unique WWN addresses of the FC HBA and its targets (storage systems). A major advantage of WWN zoning is its flexibility. If an administrator moves a node to another switch port in the fabric, the node maintains connectivity to its zone partners without having to modify the zone configuration. This is possible because the WWN is static to the node port.
  Port zoning: It uses the switch port ID to define zones. In port zoning, access to node is determined by the physical switch port to which a node is connected. The zone members are the port identifiers (switch domain ID and port number) to which FC HBA and its targets (storage systems) are connected. If a node is moved to another switch port in the fabric, port zoning must be modified to allow the node, in its new port, to participate in its original zone. However, if an FC HBA or storage system port fails, an administrator just has to replace the failed device without changing the zoning configuration.
  Mixed zoning: It combines the qualities of both WWN zoning and port zoning. Using mixed zoning enables a specific node port to be tied to the WWN of another node.
The figure on the slide shows three types of zoning on an FC network.

## Slide 112: Lesson 4: Summary
During this lesson the following topics were covered:
Single-switch topology
Mesh topology
Core-edge topology
Link aggregation
Types of zoning
Notes: This lesson covered FC SAN topologies such as single-switch, mesh, and core-edge. This lesson also covered link aggregation and types of zoning.

## Slide 113: Lesson 5: Virtualization in FC SAN
This lesson covers the following topics:
Port virtualization
  N_Port ID virtualization (NPIV)
  N_Port virtualization (NPV)
Block-level storage virtualization
Virtual SAN
Notes: This lesson covers port virtualization that comprises both N_Port ID virtualization (NPIV) and N_Port virtualization (NPV). This lesson also covers block-level storage virtualization and virtual SAN.

## Slide 114: N_Port ID Virtualization (NPIV)
A single N_Port functions as multiple virtual N_Ports
  Each virtual N_Port has a unique WWPN and FC address in FC SAN
Hypervisors leverage NPIV to create virtual N_Ports on HBA
  A virtual N_Port acts as a virtual FC HBA port that is used by a VM
  Enables zoning and LUN masking at VM level
Physical HBA
FC Switch
LUN
LUN
LUN
Virtual HBAs
Storage System
Compute System
Notes: N_Port ID virtualization (NPIV) enables a single N_Port (such as an FC HBA port) to function as multiple virtual N_Ports. Each virtual N_Port has a unique WWPN identity in the FC SAN. This allows a single physical N_Port to obtain multiple FC addresses. Hypervisors leverage NPIV to create virtual N_Ports on the FC HBA and then assign the virtual N_Ports to virtual machines (VMs). A virtual N_Port acts as a virtual FC HBA port. This enables a VM to directly access LUNs assigned to it (see the figure on the slide).
NPIV enables an administrator to restrict access to specific LUNs to specific VMs using security techniques like zoning and LUN masking; similarly to the assignment of a LUN to a physical compute system. To enable NPIV, both the FC HBAs and the FC switches must support NPIV. The physical FC HBAs on the compute system, using their own WWNs, must have access to all LUNs that are to be accessed by VMs running on that compute system.

## Slide 115: N_Port Virtualization (NPV)
NPV supported switch functions as a pass-through device
  Does not require domain ID
  Does not perform fabric services
Solves domain ID explosion problem in a fabric
Edge Switches in NPV mode
FC Director at Core
Storage System
N_Port
F_Port
N_Port
N_Port
N_Port
N_Port
F_Port
F_Port
F_Port
F_Port
F_Port
F_Port
F_Port
F_Port
NP_Port
NP_Port
NP_Port
NP_Port
Compute Systems
Notes: The proliferation of compute systems in a data center causes increased use of edge switches in a fabric. As the edge switch population grows, the number of domain IDs may become a concern because of the limitation on the number of domain IDs in a fabric. N_Port virtualization (NPV) addresses this concern by reducing the number of domain IDs in a fabric. Edge switches supporting NPV do not require a domain ID. They pass traffic between the core switch and the compute systems. NPV-enabled edge switches do not perform any fabric services, and instead forward all fabric activity, such as login and name server registration to the core switch.
All ports at the NPV edge switches that connect to the core switch are established as NP_Ports (not E_Ports). The NP_Ports connect to an NPIV-enabled core director or switch. If the core director or switch is not NPIV-capable, the NPV edge switches do not function. As the switch enters or exits from NPV mode, the switch configuration is erased and it reboots. Therefore, administrators should take care when enabling or disabling NPV on a switch. The figure on the slide shows a core-edge fabric that comprises two edge switches in NPV mode and one core switch (an FC director).

## Slide 116: Block-level Storage Virtualization
Provides a virtualization layer in SAN
  Abstracts block-based storage systems
  Aggregates LUNs to create storage pool
Virtual volumes from storage pool are assigned to compute systems
  Virtualization layer maps virtual volumes to LUNs
Benefits:
  Online expansion of virtual volumes
  Non-disruptive data migration
Virtual
Volume
Storage System
Storage System
Virtualization
Appliance
Compute Systems
FC SAN
Storage Pool
LUN
LUN
LUN
LUN
Notes: Block-level storage virtualization aggregates block storage devices (LUNs) and enables provisioning of virtual storage volumes, independent of the underlying physical storage. A virtualization layer, which exists at the SAN, abstracts the identity of block-based storage systems and creates a storage pool by aggregating LUNs from the storage systems. Virtual volumes are created from the storage pool and assigned to the compute systems. Instead of being directed to the LUNs on the individual storage systems, the compute systems are directed to the virtual volumes provided by the virtualization layer. The virtualization layer maps the virtual volumes to the LUNs on the individual storage systems. The compute systems remain unaware of the mapping operation and access the virtual volumes as if they were accessing the physical storage attached to them. Typically, the virtualization layer is managed via a dedicated virtualization appliance to which the compute systems and the storage systems are connected.
The figure on the slide shows two compute systems, each of which has one virtual volume assigned. These virtual volumes are mapped to the LUNs in the storage systems. When an I/O is sent to a virtual volume, it is redirected to the mapped LUNs through the virtualization layer at the FC SAN. Depending on the capabilities of the virtualization appliance, the architecture may allow for more complex mapping between the LUNs and the virtual volumes.
Block-level storage virtualization enables extending the virtual volumes non-disruptively to meet application’s capacity scaling requirements. It also provides the advantage of non-disruptive data migration. In a traditional SAN environment, LUN migration from one storage system to another is an offline event. After migration, the compute systems are updated to reflect the new storage system configuration. In other instances, processor cycles at the compute system were required to migrate data from one storage system to the other, especially in a multivendor environment. With a block-level storage virtualization solution in place, the virtualization layer handles the migration of data, which enables LUNs to remain online and accessible while data is migrating. No physical changes are required because the compute system still points to the same virtual volume on the virtualization layer. However, the mapping information on the virtualization layer should be changed. These changes can be executed dynamically and are transparent to the end user.

## Slide 117: Use Case: Storage Virtualization Across Data Centers
Data Center 1
Virtualization Layer
Virtualization Appliance
Compute Systems
Storage System
Virtual
Volumes
FC SAN
Compute Systems
Storage System
Virtual
Volumes
FC SAN
FC or IP
Data Center 2
Concurrent Access
to the Shared Volumes
Notes: The use case is based on the block-level storage virtualization across data centers that allow compute systems at different locations to share and concurrently access same virtual volume. According to the use case, two data centers are separated by geographic distance (see the figure on the slide). Each data center includes an FC SAN infrastructure that supports block-level storage virtualization through the deployment of the virtualization appliance. The storage virtualization solution provides the capability to connect the virtualization appliances at the two data centers. The connected virtualization appliances are managed centrally and work as a single virtualization layer stretched across the data centers. This enables the pooling of LUNs across data centers. Virtual volumes are created from the storage pool. These virtual volumes are accessible from both the data centers. Compute systems at both the data centers can perform I/O operations to these shared volumes concurrently. This enables real-time data collaboration over distance, which is a key requirement for big data applications.

## Slide 118: Virtual SAN (VSAN)/Virtual Fabric
Each VSAN has its own fabric services, configuration, and set of FC addresses
VSANs improve SAN security, scalability, availability, and manageability
Storage System
Storage System
Compute Systems
VSAN 20
VSAN 10
Compute Systems
FC SAN
A logical fabric on an FC SAN, enabling communication among a group of nodes, regardless of their physical location in the fabric.
VSAN
Notes: Virtual SAN (also called virtual fabric) is a logical fabric on an FC SAN, which enables communication among a group of nodes regardless of their physical location in the fabric. In a VSAN, a group of node ports communicate with each other using a virtual topology defined on the physical SAN. Multiple VSANs may be created on a single physical SAN. Each VSAN behaves and is managed as an independent fabric. Each VSAN has its own fabric services, configuration, and set of FC addresses. Fabric-related configurations in one VSAN do not affect the traffic in another VSAN. A VSAN may be extended across sites, enabling communication among a group of nodes, in either site with a common set of requirements.
VSANs improve SAN security, scalability, availability, and manageability. VSANs provide enhanced security by isolating the sensitive data in a VSAN and by restricting the access to the resources located within that VSAN. For example, a cloud provider typically isolates the storage pools for multiple cloud services by creating multiple VSANs on an FC SAN. Further, the same FC address can be assigned to nodes in different VSANs, thus increasing the fabric scalability. The events causing traffic disruptions in one VSAN are contained within that VSAN and are not propagated to other VSANs. VSANs facilitate an easy, flexible, and less expensive way to manage networks. Configuring VSANs is easier and quicker compared to building separate physical FC SANs for various node groups. To regroup nodes, an administrator simply changes the VSAN configurations without moving nodes and recabling.

## Slide 119: VSAN Configuration
Define VSANs on fabric switch with specific VSAN IDs
Assign VSAN IDs to F_Ports to include them in the VSANs
An N_Port connecting to an F_Port in a VSAN becomes a member of that VSAN
Switch forwards FC frames between F_Ports that belong to the same VSAN
Notes: To configure VSANs on a fabric, an administrator first needs to define VSANs on fabric switches. Each VSAN is identified with a specific number called VSAN ID. The next step is to assign a VSAN ID to the F_Ports on the switch. By assigning a VSAN ID to an F_Port, the port is included in the VSAN. In this manner, multiple F_Ports can be grouped into a VSAN. For example, an administrator may group switch ports (F_Ports) 1 and 2 into VSAN 10 (ID) and ports 6 to 12 into VSAN 20 (ID). If an N_Port connects to an F_Port that belongs to a VSAN, it becomes a member of that VSAN. The switch transfers FC frames between switch ports that belong to the same VSAN.
Note: VSAN versus Zone
Both VSANs and zones enable node ports within a fabric to be logically segmented into groups. But they are not same and their purposes are different. There is a hierarchical relationship between them. An administrator first assigns physical ports to VSANs and then configures independent zones for each VSAN. A VSAN has its own independent fabric services, but the fabric services are not available on a per-zone basis.

## Slide 120: VSAN Trunking
Allows network traffic from multiple VSANs to traverse a single ISL (trunk link)
Enables an E_Port (trunk port) to send or receive multiple VSAN traffic over a trunk link
Reduces the number of ISLs between switches configured with multiple VSANs
VSAN 10 Traffic
VSAN 20 Traffic
VSAN 30 Traffic
Without VSAN Trunking
VSAN 10,20,30
VSAN 10,20,30
FC Switch
FC Switch
Trunk link (VSAN 10, 20, 30 traffic)
With VSAN Trunking
VSAN 10,20,30
VSAN 10,20,30
FC Switch
FC Switch
Notes: VSAN trunking allows network traffic from multiple VSANs to traverse a single ISL. It supports a single ISL to permit traffic from multiple VSANs along the same path. The ISL through which multiple VSAN traffic travels is called a trunk link. VSAN trunking enables a single E_Port to be used for sending or receiving traffic from multiple VSANs over a trunk link. The E_Port capable of transferring multiple VSAN traffic is called a trunk port. The sending and receiving switches must have at least one trunk E_Port configured for all of or a subset of the VSANs defined on the switches.
VSAN trunking eliminates the need to create dedicated ISL(s) for each VSAN. It reduces the number of ISLs when the switches are configured with multiple VSANs. As the number of ISLs between the switches decreases, the number of E_Ports used for the ISLs also reduces. By eliminating needless ISLs, the utilization of the remaining ISLs increases. The complexity of managing the FC SAN is also minimized with a reduced number of ISLs.
The figure on the slide shows a VSAN trunking configuration contrasted with a network configuration without VSAN trunking. In both the cases, the switches have VSAN 10, VSAN 20, and VSAN 30 configured. If VSAN trunking is not used, three ISLs are required to transfer traffic between the three distinct VSANs. When trunking is configured, a single ISL is used to transfer all VSAN traffic.

## Slide 121: VSAN Tagging
Helps isolate FC frames from multiple VSANs that travel through and share a trunk link
ISL carries tagged traffic from multiple VSANs
VSAN tags are added to FC frames before transmitting through trunk link
Storage System
Compute System
FC Switch
Storage System
Compute System
FC Switch
VSAN 10 Traffic
VSAN 20 Traffic
VSAN 10 Traffic
VSAN 20 Traffic
VSAN 20 Traffic
VSAN 10 Traffic
Trunk Link
VSAN tags are removed when FC frames exit trunk link
A process of adding or removing a tag to the FC frames that contains VSAN-specific information.
VSAN Tagging
Notes: VSAN tagging is the process of adding or removing a marker or tag to the FC frames that contains VSAN-specific information. Associated with VSAN trunking, it helps isolate FC frames from multiple VSANs that travel through and share a trunk link. Whenever an FC frame enters an FC switch, it is tagged with a VSAN header indicating the VSAN ID of the switch port (F_Port) before sending the frame down to a trunk link. The receiving FC switch reads the tag and forwards the frame to the destination port that corresponds to that VSAN ID. The tag is removed once the frame leaves a trunk link to reach an N_Port.

## Slide 122: Lesson 5: Summary
During this lesson the following topics were covered:
N_Port ID virtualization (NPIV)
N_Port virtualization (NPV)
Block-level storage virtualization
Virtual SAN
Notes:   This lesson covered N_Port ID virtualization (NPIV), N_Port virtualization (NPV), block-level storage virtualization, and virtual SAN.

## Slide 123: Module 6: Summary
Key points covered in this module:
Third platform requirements for SAN and software-defined networking
FC SAN components and connectivity options
FC protocol stack, FC addressing, fabric services, flow control
Fabric topologies, link aggregation, and types of zoning
NPIV, NPV, block-level storage virtualization, and virtual SAN
Notes: This module covered third platform requirements for SAN and software-defined networking. It also covered FC SAN components – network adapters, cables, and interconnecting devices; FC connectivity options – point-to-point, FC-AL, FC-SW; and fabric port types such as N_Port, E_Port, F_Port, and G_Port. It includes FC protocol stack and addressing, structure and organization of FC data, fabric services, login types, and flow control. This module also covered fabric topologies – single-switch, mesh, and core-edge; link aggregation; types of zoning – WWN, port, and mixed; port virtualization – NPIV and NPV; block-level storage virtualization; and virtual SAN.